## Slide 1
Chemical
Engineering
Core Concepts
With Equations, Diagrams & Key Formulas
114 Topics
from Fundamentals to Advanced

## Slide 2
01 / 114
Numerical Methods
Iterative Solutions of Nonlinear Equations
Find roots of nonlinear equations f(x)=0 using iterative methods. Convergence when |xₙ₊₁ − xₙ| < ε.
KEY POINTS
1 Newton-Raphson: quadratic convergence 2 Bisection: robust but slow 3 Convergence tolerance ε ~10⁻⁶ 4 Excel Solver for multi-variable systems
FORMULA REFERENCE
Newton-Raphson: quadratic convergence
Bisection: robust but slow
Chemical Engineering Core Concepts
Iterative Solutions of Nonlinear Equations

## Slide 3
02 / 114
Fluid Statics
Manometry
Measure pressure differences using manometer height differences and fluid densities. Multi-fluid analysis uses sequential pressure additions.
1
U-tube: ΔP = (ρ_man − ρ_fluid)·g·h
2
Multi-fluid: add each ρgh term
3
Gauge pressure = absolute − atmospheric
4
Inclined manometers amplify sensitivity
Chemical Engineering Core Concepts
Manometry

## Slide 4
03 / 114
Process Fundamentals
Material Balances
Apply conservation of mass to chemical process streams. Steady-state with no reaction: input equals output.
Choose system boundary carefully
Steady-state: dM/dt = 0
Tie components simplify calculations
Basis = 100 mol or 100 kg typically
FORMULA
Ṁᵢₙ − Ṁₒᵤₜ + Ṁ_gen − Ṁ_consump = dM/dt
Chemical Engineering Core Concepts
Material Balances

## Slide 5
04 / 114
Process Analysis
Degrees of Freedom
Count unknowns vs. independent equations before solving. DOF = 0 means the system is fully specified.
KEY POINTS
1 List all stream variables 2 Count independent equations 3 DOF > 0: need more specifications 4 DOF < 0: redundant or inconsistent
FORMULA REFERENCE
List all stream variables
Count independent equations
Chemical Engineering Core Concepts
Degrees of Freedom

## Slide 6
05 / 114
Process Design
Recycle Mass Balances
Solve recycle loops by writing overall and per-unit balances. Overall conversion can be much higher than single-pass conversion.
1
Cut the recycle: write overall balance first
2
Per-pass conversion < overall conversion
3
Recycle ratio R = recycle/product
4
Tear stream approach in simulation
Chemical Engineering Core Concepts
Recycle Mass Balances

## Slide 7
06 / 114
Stoichiometry
Chemical Reactions
Track moles of each species using stoichiometric coefficients and extent of reaction ξ. Negative νᵢ for reactants.
νᵢ > 0 products, νᵢ < 0 reactants
Limiting reactant: ξ_max = n₀/|ν|_limiting
Conversion X = −Δn_A / n_A₀
Yield = moles desired / moles if no side rxn
FORMULA
nᵢ = nᵢ₀ + νᵢ · ξ
Chemical Engineering Core Concepts
Chemical Reactions

## Slide 8
07 / 114
Reaction Balances
Reactive Material Balances
Incorporate chemical reactions into process balances using molecular species balance or atomic species balance methods.
KEY POINTS
1 Molecular: write balance per compound 2 Atomic: atoms conserved always 3 Extent approach: one ξ per reaction 4 Independent reactions = rank of stoich. matrix
FORMULA REFERENCE
Molecular: write balance per compound
Atomic: atoms conserved always
Chemical Engineering Core Concepts
Reactive Material Balances

## Slide 9
08 / 114
Process Design
Purge Stream in Recycle Systems
Add a purge stream to prevent inert buildup in recycle loops. At steady state, purge rate equals inert feed rate.
1
Without purge: inerts accumulate indefinitely
2
Purge-to-recycle ratio set by economics
3
Lower purge → higher recycle costs
4
Inert steady-state: ṅ_purge·y_inert = ṅ_inert,feed
Chemical Engineering Core Concepts
Purge Stream in Recycle Systems

## Slide 10
09 / 114
Dynamic Systems
Material Balances on Transient Processes
Set up and solve ODEs for unsteady-state mass accumulation — tank filling, draining, semibatch mixing.
Accumulation = net input rate
Separate variables for constant rates
ODE solver for variable flow rates
Initial condition m(0) = m₀ required
FORMULA
dm/dt = ṁᵢₙ − ṁₒᵤₜ
Chemical Engineering Core Concepts
Material Balances on Transient Processes

## Slide 11
10 / 114
Composition Measurement
Wet and Dry Basis
Convert between wet basis (includes moisture) and dry basis (moisture-free reference) compositions for drying and combustion analysis.
KEY POINTS
1 Wet basis: all components incl. water 2 Dry basis: reference without moisture 3 Critical in flue gas analysis 4 Orsat analyzer reports dry basis
FORMULA REFERENCE
Wet basis: all components incl. water
Dry basis: reference without moisture
Chemical Engineering Core Concepts
Wet and Dry Basis

## Slide 12
11 / 114
Combustion Engineering
Combustion Reactions
Calculate flue gas compositions and air-to-fuel ratios. Excess air ensures complete combustion; too much cools the flame.
1
Complete: all C→CO₂, H→H₂O
2
Theoretical air: % excess = 0
3
Higher excess air → lower efficiency
4
Stack O₂ measures actual excess
Chemical Engineering Core Concepts
Combustion Reactions

## Slide 13
12 / 114
Gas Phase Systems
Ideal Gas Law
The ideal gas law relates pressure, volume, moles, and temperature. Valid at low pressure and high temperature where intermolecular forces are negligible.
Molar volume at STP: 22.4 L/mol
Compressibility factor Z = PV/nRT = 1 ideal
Dalton's Law: P_total = Σ Pᵢ (partial P)
Fails near critical point
FORMULA
PV = nRT
Chemical Engineering Core Concepts
Ideal Gas Law

## Slide 14
13 / 114
Real Gas Behavior
Equations of State
Cubic equations of state predict PVT behavior of real gases and liquids. The Peng-Robinson EOS is standard in petroleum engineering.
KEY POINTS
1 vdW: first cubic EOS (1873) 2 SRK: improved α(T) function 3 PR EOS: best for liquid density 4 Z³ − (1−B)Z² + (A−3B²−2B)Z − (AB−B²−B³) = 0
FORMULA REFERENCE
vdW: first cubic EOS (1873)
SRK: improved α(T) function
Chemical Engineering Core Concepts
Equations of State

## Slide 15
14 / 114
Phase Diagrams
Lever Rule
Determine vapor and liquid fractions in a two-phase region using the lever rule — a material balance on a phase diagram tie line.
1
V = vapor fraction, L = liquid fraction
2
V + L = 1 (total balance)
3
z = overall composition (feed)
4
Works on Pxy, Txy, and ternary diagrams
Chemical Engineering Core Concepts
Lever Rule

## Slide 16
15 / 114
Phase Diagrams
Single-Component Phase Equilibrium
Identify equilibrium phases and conditions using single-component PT diagrams. The Gibbs phase rule governs the number of independent variables.
C = components, P = phases
Single component: C = 1
Two phases: F = 1 (T or P fixes state)
Triple point: F = 0 (unique T and P)
FORMULA
Gibbs Phase Rule: F = C − P + 2
Chemical Engineering Core Concepts
Single-Component Phase Equilibrium

## Slide 17
16 / 114
Vapor Pressure
Clausius-Clapeyron & Antoine Equations
Estimate vapor pressure as a function of temperature using Antoine constants (tabulated) or the Clausius-Clapeyron integrated form.
KEY POINTS
1 Antoine: 3-parameter empirical fit 2 Clausius-Clapeyron: d(lnP)/d(1/T) = −ΔHvap/R 3 Valid over limited T range (check bounds) 4 NIST Chemistry WebBook for constants
FORMULA REFERENCE
Antoine: 3-parameter empirical fit
Clausius-Clapeyron: d(lnP)/d(1/T) = −ΔHvap/R
Chemical Engineering Core Concepts
Clausius-Clapeyron & Antoine Equations

## Slide 18
17 / 114
Vapor-Liquid Equilibrium
Raoult's Law and VLE
Model VLE for ideal solutions with Raoult's Law. Construct Pxy and Txy diagrams and perform bubble/dew point calculations.
1
Bubble point: all liquid just starts to vaporize
2
Dew point: all vapor just starts to condense
3
Relative volatility α₁₂ = P₁ˢᵃᵗ/P₂ˢᵃᵗ
4
Txy: bubble T < dew T at same composition
Chemical Engineering Core Concepts
Raoult's Law and VLE

## Slide 19
18 / 114
Solution Chemistry
Solids in Solution & Colligative Properties
Dissolved solutes lower freezing point, raise boiling point, and create osmotic pressure — all proportional to solute molality.
Kb (water) = 0.512 °C·kg/mol
Kf (water) = 1.86 °C·kg/mol
Osmotic π = iMRT
i > 1 for electrolytes (dissociation)
FORMULA
ΔTb = Kb·m·i
Chemical Engineering Core Concepts
Solids in Solution & Colligative Properties

## Slide 20
19 / 114
Three-Component Systems
Ternary Phase Diagrams
Represent three-component mixtures on equilateral triangles. Two-phase regions bounded by binodal curve; tie lines connect equilibrium phases.
KEY POINTS
1 Each vertex = pure component 2 Binary pairs on each edge 3 Plait point = critical composition 4 Used in liquid-liquid extraction design
FORMULA REFERENCE
Each vertex = pure component
Binary pairs on each edge
Chemical Engineering Core Concepts
Ternary Phase Diagrams

## Slide 21
20 / 114
Humidity & Drying
Water-Air VLE & Psychrometric Chart
Characterize moist air using humidity ratio and the psychrometric chart. Critical for drying, HVAC, and cooling tower design.
1
Dry-bulb T: regular thermometer
2
Wet-bulb T: evaporative cooling limit
3
Dew point: T where condensation begins
4
Adiabatic saturation line on psych chart
Chemical Engineering Core Concepts
Water-Air VLE & Psychrometric Chart

## Slide 22
21 / 114
Surface Separations
Adsorption
Model gas/liquid adsorption onto solid surfaces using Langmuir (monolayer) or Freundlich (empirical) isotherms for adsorbent design.
q = loading [mol/g], C = concentration
q_m = monolayer capacity
K = Langmuir equilibrium constant
Freundlich: q = K·C^(1/n) (empirical)
FORMULA
q = q_m·K·C/(1+K·C)
Chemical Engineering Core Concepts
Adsorption

## Slide 23
22 / 114
Thermodynamic Foundations
State Functions
State functions like U, H, S, G depend only on the current state, not how you got there. Path functions Q and W depend on the process.
KEY POINTS
1 State: P, T, V, U, H, S, G, A 2 Path: Q (heat), W (work) 3 dU = exact differential → closed loop = 0 4 Foundation for all thermodynamic calculations
FORMULA REFERENCE
State: P, T, V, U, H, S, G, A
Path: Q (heat), W (work)
Chemical Engineering Core Concepts
State Functions

## Slide 24
23 / 114
Water Properties
Steam Tables
Look up thermodynamic properties of water from saturated and superheated steam tables using temperature, pressure, or quality as inputs.
1
Saturated tables: f = liquid, g = vapor
2
Superheated: T > T_sat at given P
3
Quality x = mass fraction vapor (0 to 1)
4
NIST REFPROP or textbook appendices
Chemical Engineering Core Concepts
Steam Tables

## Slide 25
24 / 114
Piping Systems
Mechanical Energy Balance
Extended Bernoulli equation accounts for pump/turbine work and friction losses for real piping system design.
h_p = Ẇ_pump/(ṁg) pump head
h_f = f(L/D)(v²/2g) Darcy friction
NPSH: prevent cavitation in pumps
System curve intersects pump curve at operating point
FORMULA
P₁/ρg + v₁²/2g + z₁ + h_p = P₂/ρg + v₂²/2g + z₂ + h_f
Chemical Engineering Core Concepts
Mechanical Energy Balance

## Slide 26
25 / 114
Thermal Properties
Heat Capacities
Use heat capacity correlations to calculate enthalpy and internal energy changes for gases, liquids, and solids across temperature ranges.
KEY POINTS
1 Cp − Cv = R for ideal gases 2 Cp/Cv = γ (adiabatic index) 3 Shomate eq: a,b,c,d from NIST 4 Mean heat capacity simplifies integrals
FORMULA REFERENCE
Cp − Cv = R for ideal gases
Cp/Cv = γ (adiabatic index)
Chemical Engineering Core Concepts
Heat Capacities

## Slide 27
26 / 114
Latent Heat
Energy Balances with Phase Changes
Construct enthalpy paths through phase changes by combining sensible heat (Cp·ΔT) and latent heat steps.
1
Construct path: heat → phase change → heat
2
ΔHvap water = 2257 kJ/kg at 100°C
3
ΔHfus water = 334 kJ/kg at 0°C
4
Trouton's rule: ΔHvap/Tb ≈ 88 J/mol·K
Chemical Engineering Core Concepts
Energy Balances with Phase Changes

## Slide 28
27 / 114
VLE Calculations
Flash Separations
Solve flash drum calculations by finding vapor fraction V and phase compositions using K-values (Kᵢ = yᵢ/xᵢ).
Kᵢ = Pᵢˢᵃᵗ/P from Raoult's Law
V = 0: bubble point; V = 1: dew point
Rachford-Rice: monotonic → easy to solve
Iterative: guess T or P → compute V → check
FORMULA
Σyᵢ − Σxᵢ = 0 (Rachford-Rice)
Chemical Engineering Core Concepts
Flash Separations

## Slide 29
28 / 114
Reaction Thermodynamics
Heats of Reaction
Calculate standard heats of reaction from heats of formation. Exothermic: ΔH < 0, heat released. Endothermic: ΔH > 0, heat absorbed.
KEY POINTS
1 ΔH°f for elements in standard state = 0 2 Kirchhoff: ΔHrxn(T) = ΔH°rxn + ∫ΔCp dT 3 Hess's Law: combine known reactions 4 Bond energies give approximate ΔHrxn
FORMULA REFERENCE
ΔH°f for elements in standard state = 0
Kirchhoff: ΔHrxn(T) = ΔH°rxn + ∫ΔCp dT
Chemical Engineering Core Concepts
Heats of Reaction

## Slide 30
29 / 114
Reactor Thermodynamics
Energy Balances with Reaction
Combine sensible heat and heat of reaction in energy balances for reactive systems. Choose a reference temperature for the path.
1
Reference T: choose T_in or 25°C
2
Exothermic reactor: requires cooling
3
Adiabatic: Q = 0, solve for T_out
4
Multiple reactions: sum ξⱼ·ΔHrxn,j
Chemical Engineering Core Concepts
Energy Balances with Reaction

## Slide 31
30 / 114
Combustion Thermodynamics
Adiabatic Flame Temperature
Maximum temperature reached in adiabatic combustion. Decreases with excess air and moisture; increases with preheating and oxygen enrichment.
Q = 0 (no heat loss)
H_reactants(Tin) = H_products(Tad)
Excess air lowers Tad significantly
Preheated air or O₂ enrichment raises Tad
FORMULA
Q = 0: ΔH_reactants = ΔH_products
Chemical Engineering Core Concepts
Adiabatic Flame Temperature

## Slide 32
31 / 114
Thermodynamics
First Law — Closed Systems (Intro)
Energy conservation for closed systems: heat added minus boundary work done equals change in internal energy.
KEY POINTS
1 Closed system: no mass flow in/out 2 Rigid vessel: W = 0 → ΔU = Q 3 Isobaric: W = PΔV 4 Sign convention: Q>0 in, W>0 out
FORMULA REFERENCE
Closed system: no mass flow in/out
Rigid vessel: W = 0 → ΔU = Q
Chemical Engineering Core Concepts
First Law — Closed Systems (Intro)

## Slide 33
32 / 114
Fluid Statics
Buoyancy
Archimedes' principle: buoyant force equals weight of fluid displaced. Objects float when buoyancy exceeds weight.
1
Fb = ρ_fluid·g·V_disp
2
Sinks: ρ_obj > ρ_fluid
3
Floats: ρ_obj < ρ_fluid (partial submersion)
4
Stable: center of buoyancy above center of gravity
Chemical Engineering Core Concepts
Buoyancy

## Slide 34
33 / 114
Fluid Mechanics Fundamentals
Properties of Fluids
Key fluid properties: density, viscosity, surface tension, and vapor pressure govern fluid behavior in all process equipment.
Dynamic viscosity μ [Pa·s or cP]
Kinematic ν = μ/ρ [m²/s or cSt]
Surface tension γ [N/m]
Vapor pressure: cavitation risk if P < Pvap
FORMULA
ν = μ/ρ (kinematic viscosity)
Chemical Engineering Core Concepts
Properties of Fluids

## Slide 35
34 / 114
Fluid Statics
Hydrostatic Pressure
Pressure in a static fluid increases linearly with depth regardless of container shape — only depth and fluid density matter.
KEY POINTS
1 P is depth-dependent only (not shape) 2 ΔP = ρgh for incompressible fluid 3 Pressure head: h = P/(ρg) 4 Multi-layer: add each ρᵢgᵢhᵢ contribution
FORMULA REFERENCE
P is depth-dependent only (not shape)
ΔP = ρgh for incompressible fluid
Chemical Engineering Core Concepts
Hydrostatic Pressure

## Slide 36
35 / 114
Fluid Statics
Submerged Gates
The resultant hydrostatic force acts at the center of pressure, which is always below the centroid of the submerged surface.
1
F = pressure at centroid × area
2
ȳ = depth to centroid
3
I_xc = second moment of area about centroid
4
y_cp > ȳ always (center of pressure deeper)
Chemical Engineering Core Concepts
Submerged Gates

## Slide 37
36 / 114
Fluid Dynamics
Bernoulli's Equation
Energy conservation for ideal fluid flow along a streamline — pressure, kinetic, and potential energy sum to a constant.
P: pressure energy per unit weight
v²/2g: velocity head
z: elevation head
Venturi: ΔP measures flow velocity
FORMULA
P/ρg + v²/2g + z = H (constant)
Chemical Engineering Core Concepts
Bernoulli's Equation

## Slide 38
37 / 114
Fluid Rheology
Viscosity and Shear Stress
Newton's law of viscosity relates shear stress to velocity gradient. Newtonian fluids have constant viscosity independent of shear rate.
KEY POINTS
1 μ = dynamic viscosity [Pa·s] 2 dv/dy = velocity gradient (shear rate) 3 Newtonian: μ constant (water, air) 4 Power law: τ = K·(dv/dy)ⁿ for non-Newtonian
FORMULA REFERENCE
μ = dynamic viscosity [Pa·s]
dv/dy = velocity gradient (shear rate)
Chemical Engineering Core Concepts
Viscosity and Shear Stress

## Slide 39
38 / 114
Fluid Mechanics
Conservation of Mass
The continuity equation ensures mass is conserved in fluid flow. For incompressible flow, volumetric flow rate is constant along a streamline.
1
Incompressible: ρ = constant
2
ṁ = ρ·A·v = constant in steady pipe flow
3
Q = A·v = volumetric flow rate
4
Contraction: smaller A → larger v
Chemical Engineering Core Concepts
Conservation of Mass

## Slide 40
39 / 114
Transport Phenomena
Introduction to Pipe Flow
Reynolds number determines the flow regime in pipes. Laminar flow is orderly; turbulent flow has chaotic mixing that enhances heat and mass transfer.
Re = inertial / viscous forces
Transition zone: 2100 < Re < 4000
Hydraulic diameter for non-circular: Dh = 4A/P
Higher Re → higher friction factor f
FORMULA
Re = ρ·v·D/μ = v·D/ν
Chemical Engineering Core Concepts
Introduction to Pipe Flow

## Slide 41
40 / 114
Velocity Profiles
Velocity in Pipe Flow
Laminar pipe flow has a parabolic velocity profile. Turbulent flow has a flatter profile with enhanced mixing near the wall.
KEY POINTS
1 v_max at centerline (r=0) 2 v = 0 at wall (no-slip condition) 3 Turbulent: v_avg ≈ 0.8 v_max 4 1/7 power law for turbulent: v/v_max = (1−r/R)^(1/7)
FORMULA REFERENCE
v_max at centerline (r=0)
v = 0 at wall (no-slip condition)
Chemical Engineering Core Concepts
Velocity in Pipe Flow

## Slide 42
41 / 114
External Flow
Boundary Layer over a Flat Surface
The boundary layer grows from zero at the leading edge. Laminar BL is thin and predictable; turbulent BL has higher drag and better heat transfer.
1
δ = boundary layer thickness
2
Re_x = ρUx/μ (local Reynolds number)
3
Cd_laminar = 1.328/√Re_L
4
Turbulent δ ∝ x^(4/5) grows faster
Chemical Engineering Core Concepts
Boundary Layer over a Flat Surface

## Slide 43
42 / 114
Developing Flow
Entrance Length in Pipe Flow
Entrance length is the distance needed for the velocity profile to fully develop from a uniform inlet. Heat transfer correlations differ in entry vs. developed regions.
Laminar: long entry (10s of diameters)
Turbulent: shorter entry (~10-60 D)
Entry region: higher Nusselt number
Fully developed: profile shape doesn't change
FORMULA
Laminar: L_e = 0.06·Re·D
Chemical Engineering Core Concepts
Entrance Length in Pipe Flow

## Slide 44
43 / 114
Pipe Design
Pressure Drop & Power in Pipe Flow
Darcy-Weisbach equation calculates frictional pressure drop. The Moody chart provides friction factor f as a function of Re and relative roughness.
KEY POINTS
1 Friction factor f from Moody chart 2 Laminar: f = 64/Re (exact) 3 Turbulent: Colebrook-White equation 4 ε/D = relative roughness (ε = pipe roughness)
FORMULA REFERENCE
Friction factor f from Moody chart
Laminar: f = 64/Re (exact)
Chemical Engineering Core Concepts
Pressure Drop & Power in Pipe Flow

## Slide 45
44 / 114
Minor Losses
Equivalent Length in Pipe Systems
Convert minor losses from fittings (elbows, valves, tees) into equivalent pipe lengths for unified pressure drop calculations.
1
K values tabulated for fittings
2
Gate valve fully open: K ≈ 0.2
3
90° elbow: K ≈ 0.9
4
Total h_f = Darcy ΔP + Σ minor losses
Chemical Engineering Core Concepts
Equivalent Length in Pipe Systems

## Slide 46
45 / 114
Pipe Networks
Multipipe Systems
Analyze networks of pipes in series (same flow, additive pressure drop) or parallel (same pressure drop, additive flow rates).
Series: bottleneck at highest resistance
Parallel: flow distributes by resistance
Hardy-Cross: iterative network solver
Pump location affects network behavior
FORMULA
Series: Q same, ΔP = Σ ΔPᵢ
Chemical Engineering Core Concepts
Multipipe Systems

## Slide 47
46 / 114
Fluid Dynamics
Linear Momentum
Apply Newton's second law as the linear momentum equation to find forces on pipe bends, nozzles, and impinging jets.
KEY POINTS
1 Control volume momentum balance 2 Include ALL forces: pressure, gravity, reaction 3 Pipe bend: compute Fx and Fy separately 4 Jet force: F = ρQ(v_out − v_in)
FORMULA REFERENCE
Control volume momentum balance
Include ALL forces: pressure, gravity, reaction
Chemical Engineering Core Concepts
Linear Momentum

## Slide 48
47 / 114
Navier-Stokes Reduction
Pressure Field & Fluid at Rest
The Navier-Stokes equation simplifies to ∇P = ρg for a stationary fluid, directly giving the hydrostatic pressure distribution.
1
N-S: ρ(Dv/Dt) = −∇P + μ∇²v + ρg
2
Static: Dv/Dt = 0, μ∇²v = 0
3
Result: dP/dz = −ρg (hydrostatics)
4
Horizontal: dP/dx = dP/dy = 0
Chemical Engineering Core Concepts
Pressure Field & Fluid at Rest

## Slide 49
48 / 114
Analytical Solutions
Velocity Profiles from Navier-Stokes
Solve N-S equations with no-slip boundary conditions to derive exact velocity profiles for laminar flows in simple geometries.
No-slip: v = 0 at wall always
Poiseuille flow: pipe, pressure-driven
Couette flow: between plates, shear-driven
Parabolic profile → Q = πR⁴ΔP/(8μL)
FORMULA
Poiseuille: v(r) = (R²−r²)/(4μ)·(−dP/dz)
Chemical Engineering Core Concepts
Velocity Profiles from Navier-Stokes

## Slide 50
49 / 114
Similarity Theory
Dimensional Analysis & Pi Terms
Buckingham Pi theorem reduces the number of variables needed to describe a phenomenon by grouping them into dimensionless Pi numbers.
KEY POINTS
1 7 base units: M, L, T, Θ, I, N, J 2 Re = ρvL/μ (inertia/viscous) 3 Fr = v/√(gL) (inertia/gravity) 4 Nu = hL/k (convection/conduction)
FORMULA REFERENCE
7 base units: M, L, T, Θ, I, N, J
Re = ρvL/μ (inertia/viscous)
Chemical Engineering Core Concepts
Dimensional Analysis & Pi Terms

## Slide 51
50 / 114
Scale-Up Methods
Modeling and Similitude
Design scale model experiments by matching relevant dimensionless numbers. Full similitude requires geometric, kinematic, and dynamic similarity.
1
Geometric: same shape (scale factor λ)
2
Kinematic: same velocity ratios
3
Dynamic: same Re, Fr, We etc.
4
Often impossible to match all simultaneously
Chemical Engineering Core Concepts
Modeling and Similitude

## Slide 52
51 / 114
Thermodynamics
First Law — Closed Systems
The first law of thermodynamics for a closed system: change in internal energy equals heat transferred to the system minus work done by the system.
Isochoric (const. V): W = 0, ΔU = Q
Isobaric (const. P): W = PΔV, Q = nCpΔT
Isothermal ideal gas: ΔU = 0, Q = W
Adiabatic: Q = 0, ΔU = −W
FORMULA
ΔU = Q − W
Chemical Engineering Core Concepts
First Law — Closed Systems

## Slide 53
52 / 114
Steady-State Energy Balance
First Law — Open Systems
For steady-state open systems (turbines, pumps, nozzles, heat exchangers), the energy balance includes enthalpy, kinetic, and potential energy terms.
KEY POINTS
1 Turbines: work out, Ẇs < 0 2 Compressors: work in, Ẇs > 0 3 Nozzle: ΔKE = −ΔĤ (Q=0, Ẇ=0) 4 Heat exchanger: Ẇ = 0, Δ(ṁh) = Q̇
FORMULA REFERENCE
Turbines: work out, Ẇs < 0
Compressors: work in, Ẇs > 0
Chemical Engineering Core Concepts
First Law — Open Systems

## Slide 54
53 / 114
Transient Thermodynamics
Unsteady Energy Balances on Tanks
Track energy accumulation in a tank being filled or drained — the internal energy of the system changes with time.
1
Filling from supply: T rises if h_supply > u_tank
2
Draining: tank cools if adiabatic
3
Rigid tank assumption simplifies analysis
4
Solve ODE: dU/dt = ṁᵢₙhᵢₙ for filling
Chemical Engineering Core Concepts
Unsteady Energy Balances on Tanks

## Slide 55
54 / 114
Second Law of Thermodynamics
Entropy
Entropy is a state function that measures irreversibility. The entropy of the universe always increases for any real process.
Reversible: ΔS_univ = 0
Irreversible: ΔS_univ > 0
ΔS ideal gas = nCv·ln(T₂/T₁) + nR·ln(V₂/V₁)
Entropy generation = source of lost work
FORMULA
dS ≥ δQ/T (Clausius inequality)
Chemical Engineering Core Concepts
Entropy

## Slide 56
55 / 114
Work Devices
Turbines and Compressors
Isentropic efficiency compares actual device performance to the ideal reversible adiabatic case. Turbines produce work; compressors consume work.
KEY POINTS
1 Isentropic: adiabatic + reversible 2 Turbine: ηT = (h₁−h₂)/(h₁−h₂s) 3 Compressor: ηC = (h₂s−h₁)/(h₂−h₁) 4 Intercooling reduces compressor work
FORMULA REFERENCE
Isentropic: adiabatic + reversible
Turbine: ηT = (h₁−h₂)/(h₁−h₂s)
Chemical Engineering Core Concepts
Turbines and Compressors

## Slide 57
56 / 114
Work Analysis
Reversible & Irreversible Expansion/Compression
Reversible processes produce maximum work (or require minimum work). Irreversibility always increases the work input required for compression.
1
Isothermal reversible: W = nRT·ln(V₂/V₁)
2
Adiabatic rev.: W = ΔU = nCv(T₂−T₁)
3
Irreversible: gas expands against P_ext
4
Polytropic: PVⁿ = const (n between 1 and γ)
Chemical Engineering Core Concepts
Reversible & Irreversible Expansion/Compression

## Slide 58
57 / 114
Isentropic Processes
Adiabatic Reversible Expansion/Compression
Isentropic processes follow PVᵞ = const for ideal gases. Used for turbine/compressor outlet calculations and acoustic wave analysis.
γ = 1.4 for diatomic gases (N₂, O₂, air)
γ = 1.67 for monatomic (Ar, He)
W = Cv(T₂−T₁) per mole
Steam: use steam tables (not ideal gas law)
FORMULA
T₂/T₁ = (P₂/P₁)^((γ−1)/γ)
Chemical Engineering Core Concepts
Adiabatic Reversible Expansion/Compression

## Slide 59
58 / 114
Ideal Power Cycle
Carnot Cycle
The Carnot cycle sets the maximum possible efficiency for a heat engine operating between two temperature reservoirs.
KEY POINTS
1 4 reversible steps: 2 isothermal + 2 adiabatic 2 η depends only on T_H and T_L [Kelvin] 3 No real engine exceeds Carnot efficiency 4 Higher T_H or lower T_L → better efficiency
FORMULA REFERENCE
4 reversible steps: 2 isothermal + 2 adiabatic
η depends only on T_H and T_L [Kelvin]
Chemical Engineering Core Concepts
Carnot Cycle

## Slide 60
59 / 114
Steam Power Plants
Rankine Cycle
The Rankine cycle is the basis for all steam power plants. Four components: boiler, turbine, condenser, pump.
1
State 1: saturated liquid (condenser out)
2
State 2: compressed liquid (pump out)
3
State 3: superheated steam (boiler out)
4
State 4: wet steam (turbine out)
Chemical Engineering Core Concepts
Rankine Cycle

## Slide 61
60 / 114
Cooling & Heat Pumps
Refrigeration Cycle
The vapor-compression cycle moves heat from cold to hot reservoir using compressor work. COP > 1 because heat is pumped, not generated.
Compressor: raises T and P of refrigerant
Condenser: rejects heat Q_H to environment
Expansion valve: drops P (throttling)
Evaporator: absorbs Q_L from cold space
FORMULA
COP_R = Q_L / W_net
Chemical Engineering Core Concepts
Refrigeration Cycle

## Slide 62
61 / 114
Pressure Reduction
Throttling & Joule-Thomson Expansion
Throttling through a valve is isenthalpic. For real gases, temperature changes according to the Joule-Thomson coefficient μ_JT.
KEY POINTS
1 Ideal gas: ΔT = 0 (μ_JT = 0) 2 Real gas: μ_JT can be + or − 3 Inversion T: above it, gas heats on expansion 4 Used in liquefaction cycles (μ_JT > 0)
FORMULA REFERENCE
Ideal gas: ΔT = 0 (μ_JT = 0)
Real gas: μ_JT can be + or −
Chemical Engineering Core Concepts
Throttling & Joule-Thomson Expansion

## Slide 63
62 / 114
Advanced Thermodynamics
Fundamental Property Relations
Derive Maxwell relations from the four thermodynamic potentials to relate unmeasurable properties (S) to measurable ones (P, V, T).
1
dU = TdS − PdV
2
dH = TdS + VdP
3
dA = −SdT − PdV
4
dG = −SdT + VdP
Chemical Engineering Core Concepts
Fundamental Property Relations

## Slide 64
63 / 114
Cryogenic Engineering
Liquefaction
Liquefy gases by cooling below inversion temperature then throttling. The Claude cycle uses expansion turbines for pre-cooling to improve efficiency.
Must cool gas below inversion T first
Linde: simple, low efficiency
Claude: turbine expansion → higher yield
LNG, LOX, LH₂ production methods
FORMULA
Linde: throttle below inversion T
Chemical Engineering Core Concepts
Liquefaction

## Slide 65
64 / 114
Property Charts
Thermodynamic Property Phase Diagrams
Different property diagrams provide different insights: PV for work, TS for heat and entropy, PH for refrigeration cycles.
KEY POINTS
1 PV: work = enclosed area for cycles 2 TS: heat = area; reversible cycles 3 PH (Mollier): standard for refrigerants 4 Phase envelope: bubble and dew curves
FORMULA REFERENCE
PV: work = enclosed area for cycles
TS: heat = area; reversible cycles
Chemical Engineering Core Concepts
Thermodynamic Property Phase Diagrams

## Slide 66
65 / 114
Real Gas Property Calc.
Departure Functions
Calculate real gas enthalpy and entropy by adding departure functions to ideal gas reference values using generalized correlations.
1
Departure = actual − ideal gas reference
2
Use PR EOS: H^R = RT²(∂lnφ/∂T)_P·n
3
Pitzer: H^R/(RTc) = H^R(0)/RTc + ω·H^R(1)/RTc
4
ω = acentric factor (tables for compounds)
Chemical Engineering Core Concepts
Departure Functions

## Slide 67
66 / 114
Phase Equilibrium
Fugacity of a Single Component
Fugacity is the 'corrected pressure' that accounts for non-ideal behavior. Phase equilibrium requires equal fugacities in all phases.
f → P as P → 0 (ideal gas limit)
ln(φ) = (1/RT)∫₀ᴾ(V − RT/P)dP
Fugacity coefficient φ from EOS
Poynting correction for liquids at high P
FORMULA
f = φ·P (pure component)
Chemical Engineering Core Concepts
Fugacity of a Single Component

## Slide 68
67 / 114
Mixture Thermodynamics
Partial Molar Quantities
Partial molar properties quantify how extensive mixture properties change with composition — the basis for activity coefficient models.
KEY POINTS
1 M̄ᵢ depends on T, P, and composition 2 V̄ᵢ = partial molar volume 3 Ḡᵢ = μᵢ (chemical potential) 4 Method of intercepts: graphical determination
FORMULA REFERENCE
M̄ᵢ depends on T, P, and composition
V̄ᵢ = partial molar volume
Chemical Engineering Core Concepts
Partial Molar Quantities

## Slide 69
68 / 114
Mixture Phase Equilibrium
Fugacities of Mixtures
Compute component fugacities in mixtures using equations of state with mixing rules for multi-component vapor-liquid equilibrium.
1
φ̂ᵢ = mixture fugacity coefficient
2
Mixing rules: a_mix = ΣΣxᵢxⱼaᵢⱼ
3
kᵢⱼ = binary interaction parameter
4
Used in process simulators (Aspen, HYSYS)
Chemical Engineering Core Concepts
Fugacities of Mixtures

## Slide 70
69 / 114
Equilibrium Criterion
Chemical Potential
Chemical potential is the fundamental thermodynamic driving force for mass transfer and phase/reaction equilibrium.
μᵢ = Ḡᵢ (partial molar Gibbs energy)
Mass transfers from high to low μ
μᵢ = μᵢ° + RT·ln(aᵢ) (activity aᵢ)
Reaction equilibrium: ΣνᵢμᵢT = 0
FORMULA
μᵢ = (∂G/∂nᵢ)_{T,P,nⱼ}
Chemical Engineering Core Concepts
Chemical Potential

## Slide 71
70 / 114
Activity Coefficients
VLE for Non-Ideal Solutions
Activity coefficients correct for non-ideal liquid-phase behavior. γ > 1: positive deviation (weaker interactions); γ < 1: negative deviation.
KEY POINTS
1 Margules (1 suffix): ln(γ₁) = A·x₂² 2 Wilson: good for miscible, polar systems 3 NRTL: for partially miscible systems 4 UNIFAC: group-contribution method
FORMULA REFERENCE
Margules (1 suffix): ln(γ₁) = A·x₂²
Wilson: good for miscible, polar systems
Chemical Engineering Core Concepts
VLE for Non-Ideal Solutions

## Slide 72
71 / 114
Membrane Separations
Osmosis and Reverse Osmosis
Osmotic pressure drives water through semi-permeable membranes. Applying pressure greater than π reverses the flow — the basis of RO desalination.
1
π = iMRT (van't Hoff equation)
2
Seawater π ≈ 27 bar
3
RO requires ΔP > π (30-70 bar for seawater)
4
Rejection = 1 − C_permeate/C_feed
Chemical Engineering Core Concepts
Osmosis and Reverse Osmosis

## Slide 73
72 / 114
Gas-Liquid Operations
Absorption & Henry's Law
Henry's Law describes dilute gas absorption into liquid. Column design uses number of transfer units (NTU) and height of a transfer unit (HTU).
H large: sparingly soluble (O₂ in water)
H small: highly soluble (NH₃, SO₂)
H increases with T → less soluble at high T
Column height = HTU × NTU
FORMULA
pᵢ = Hᵢ·xᵢ (Henry's Law, dilute)
Chemical Engineering Core Concepts
Absorption & Henry's Law

## Slide 74
73 / 114
Solution Non-Ideality
Enthalpy of Mixing & Raoult Deviations
Excess Gibbs energy links activity coefficients to deviations from Raoult's Law. Positive GE causes azeotrope formation at maximum-boiling azeotrope.
KEY POINTS
1 Positive deviation (γ>1): weaker A-B vs A-A, B-B 2 Negative deviation (γ<1): stronger cross interactions 3 ΔHmix ≠ 0 for non-ideal solutions 4 Excess properties: actual − ideal solution
FORMULA REFERENCE
Positive deviation (γ>1): weaker A-B vs A-A, B-B
Negative deviation (γ<1): stronger cross interactions
Chemical Engineering Core Concepts
Enthalpy of Mixing & Raoult Deviations

## Slide 75
74 / 114
Equation-of-State VLE
Cubic EOS for VLE
Use cubic EOS (Peng-Robinson) to compute fugacity coefficients in both phases for rigorous VLE calculations without activity coefficient models.
1
PR EOS gives 3 Z roots; choose correct ones
2
Smallest Z root = liquid; largest = vapor
3
φ̂ᵢ from fugacity integral of EOS
4
Iterate until φ̂^L = φ̂^V at each composition
Chemical Engineering Core Concepts
Cubic EOS for VLE

## Slide 76
75 / 114
Stability Analysis
Gibbs Free Energy & Phase Separation
Liquid-liquid phase separation occurs when the Gibbs energy of mixing has a region of negative curvature. Spinodal = instability limit; binodal = equilibrium limit.
Common tangent → binodal compositions
Inflection points → spinodal boundary
Metastable: between spinodal and binodal
Applies to polymer blends and alloys
FORMULA
∂²G_mix/∂x² < 0 → unstable
Chemical Engineering Core Concepts
Gibbs Free Energy & Phase Separation

## Slide 77
76 / 114
LLE Phase Behavior
Partially Miscible Liquids Phase Diagrams
Some liquid pairs are miscible at high T but separate into two phases at lower T (UCST) or vice versa (LCST). Tie lines give equilibrium compositions.
KEY POINTS
1 UCST: upper critical solution temperature 2 LCST: lower critical (rarer, polymer systems) 3 Two-phase region bounded by binodal curve 4 Tie lines: horizontal in T-x diagram
FORMULA REFERENCE
UCST: upper critical solution temperature
LCST: lower critical (rarer, polymer systems)
Chemical Engineering Core Concepts
Partially Miscible Liquids Phase Diagrams

## Slide 78
77 / 114
Steam Distillation
Immiscible Liquids Phase Diagrams
Immiscible liquids exert independent vapor pressures. Boiling occurs below the boiling point of either pure component — the basis of steam distillation.
1
Each liquid exerts its own P*
2
Three-phase: L₁ + L₂ + V at unique T
3
Steam distillation: purify high-bp organics
4
Heteroazeotrope at three-phase T and comp.
Chemical Engineering Core Concepts
Immiscible Liquids Phase Diagrams

## Slide 79
78 / 114
Eutectic Systems
Solid-Solid-Liquid Phase Diagrams
Binary eutectic diagrams show how two solids compete with a shared liquid phase. The eutectic point is the lowest melting composition.
Eutectic composition: lowest melting point
Hypoeutectic: left of eutectic
Hypereutectic: right of eutectic
Applications: solders, salt de-icing, alloys
FORMULA
Eutectic: L ↔ α + β at fixed T,x
Chemical Engineering Core Concepts
Solid-Solid-Liquid Phase Diagrams

## Slide 80
79 / 114
Distillation Limits
Azeotropes
Azeotropes form where vapor and liquid have identical compositions — making conventional distillation impossible beyond this point.
KEY POINTS
1 Max boiling: γ < 1 (negative deviation) 2 Min boiling: γ > 1 (positive deviation) 3 EtOH-water: min boiling at 95.6% EtOH 4 Break by adding entrainer (pressure swing, extraction)
FORMULA REFERENCE
Max boiling: γ < 1 (negative deviation)
Min boiling: γ > 1 (positive deviation)
Chemical Engineering Core Concepts
Azeotropes

## Slide 81
80 / 114
Reaction Equilibrium
Gas-Phase Chemical Equilibrium
The equilibrium constant Kp is determined by standard Gibbs energy change. Le Chatelier's principle predicts shifts due to T, P, or concentration changes.
1
Kp dimensionless (use P/P° = P/1 bar)
2
T increases Kp if endothermic (van't Hoff)
3
Pressure shifts equilibrium if Δν ≠ 0
4
Inert gas at const V: no effect on equilibrium
Chemical Engineering Core Concepts
Gas-Phase Chemical Equilibrium

## Slide 82
81 / 114
Multi-Phase Reactions
Heterogeneous Chemical Equilibrium
In heterogeneous equilibria, pure solids and liquids have unit activity and do not appear in the equilibrium expression.
CaCO₃ decomposition: Kp = P_CO₂
Only gas-phase species in Kp expression
Roasting reactions: thermite, cement
Catalytic reactions: solid catalyst (activity=1)
FORMULA
Pure solid activity = 1
Chemical Engineering Core Concepts
Heterogeneous Chemical Equilibrium

## Slide 83
82 / 114
Temperature & Equilibrium
Thermal Effects in Chemical Reactions
Temperature profoundly affects equilibrium. Exothermic reactions favor low T; endothermic favor high T. The van't Hoff equation quantifies this.
KEY POINTS
1 Exothermic (ΔH<0): Kp decreases with T 2 Endothermic (ΔH>0): Kp increases with T 3 Adiabatic T_eq: solve energy + equilibrium simultaneously 4 Ammonia synthesis: low T favors eq., high T for rate
FORMULA REFERENCE
Exothermic (ΔH<0): Kp decreases with T
Endothermic (ΔH>0): Kp increases with T
Chemical Engineering Core Concepts
Thermal Effects in Chemical Reactions

## Slide 84
83 / 114
Coupled Equilibria
Chemical Equilibrium for Multiple Reactions
For systems with multiple simultaneous reactions, minimize total Gibbs free energy subject to elemental conservation constraints.
1
Approach 1: coupled Kp equations
2
Approach 2: Gibbs minimization (more general)
3
Stoichiometry: independent reactions only
4
Software: Aspen, FactSage, GASEQ
Chemical Engineering Core Concepts
Chemical Equilibrium for Multiple Reactions

## Slide 85
84 / 114
Parameter Estimation
Nonlinear Regression
Fit kinetic rate law parameters to experimental data by minimizing the sum of squared residuals using iterative optimization.
Initial guess critical for convergence
Arrhenius: k = A·exp(−Ea/RT)
Use log-linearization for initial guess
Confidence intervals: assess parameter uncertainty
FORMULA
min Σ(y_exp − y_model)²
Chemical Engineering Core Concepts
Nonlinear Regression

## Slide 86
85 / 114
Reaction Optimization
Multiple Reactions and Selectivity
Optimize selectivity in competing reaction networks by choosing reactor type, temperature, and concentration profiles strategically.
KEY POINTS
1 Parallel: A→D (desired), A→U (undesired) 2 Series: A→D→U (minimize overreaction) 3 High CA favors higher-order desired reactions 4 CSTR vs PFR: compare CA profiles
FORMULA REFERENCE
Parallel: A→D (desired), A→U (undesired)
Series: A→D→U (minimize overreaction)
Chemical Engineering Core Concepts
Multiple Reactions and Selectivity

## Slide 87
86 / 114
Heterogeneous Catalysis
Langmuir-Hinshelwood Kinetics
Surface-catalyzed reactions follow Langmuir-Hinshelwood kinetics where adsorption, surface reaction, and desorption are sequential steps.
1
Adsorption: A + S ⇌ A·S
2
Surface rxn: A·S + B·S → P·S
3
Desorption: P·S ⇌ P + S
4
Denominator reflects competition for active sites
Chemical Engineering Core Concepts
Langmuir-Hinshelwood Kinetics

## Slide 88
87 / 114
Internal Mass Transfer
Diffusion & Reaction in Porous Catalysts
Internal diffusion through catalyst pores can limit the observed reaction rate. The Thiele modulus compares reaction to diffusion rates.
η = 1: no diffusion limitation
η < 1: diffusion limits reaction
Strong: η ≈ 1/Φ for Φ >> 1
De = effective diffusivity in pores (tortuosity)
FORMULA
Φ = R√(k/D_e) (Thiele modulus)
Chemical Engineering Core Concepts
Diffusion & Reaction in Porous Catalysts

## Slide 89
88 / 114
Reactor Design
Isothermal Batch Reactors
Design isothermal batch reactors by integrating the mole balance. Reaction time depends on rate law and desired conversion.
KEY POINTS
1 Design equation: N_A0·dX/dt = −r_A·V 2 0th order: t = CA0·X/k 3 1st order: t = −ln(1−X)/k 4 2nd order: t = X/(k·CA0·(1−X))
FORMULA REFERENCE
Design equation: N_A0·dX/dt = −r_A·V
0th order: t = CA0·X/k
Chemical Engineering Core Concepts
Isothermal Batch Reactors

## Slide 90
89 / 114
Continuous Reactor Design
Isothermal CSTR
CSTR operates at exit concentration everywhere (perfect mixing). Design equation is algebraic — evaluate rate at exit conditions.
1
τ = CA0·X/(−rA|exit)
2
CSTR less efficient than PFR for positive-order kinetics
3
Multiple CSTRs approach PFR performance
4
Levenspiel plot: CSTR area = rectangle, PFR = integral
Chemical Engineering Core Concepts
Isothermal CSTR

## Slide 91
90 / 114
Reactor Design
Isothermal Plug Flow Reactors
PFR has no axial mixing — concentration varies along the length. The integral design equation requires knowing the rate law explicitly.
Each element of fluid reacts for residence time dV/v₀
PFR < CSTR volume for positive-order reactions
Levenspiel plot: PFR = area under curve
Can handle pressure drop (coupled ODE)
FORMULA
FA₀·dX/dV = −rA
Chemical Engineering Core Concepts
Isothermal Plug Flow Reactors

## Slide 92
91 / 114
Special Reactors
Isothermal Semibatch Reactors
Semibatch reactor has one reactant charged initially, second added continuously. Useful for controlling selectivity and managing exotherms.
KEY POINTS
1 Fed-batch fermentation: add nutrients continuously 2 Control selectivity: keep CB low to favor desired product 3 Volume changes with time: dV/dt = v₀ 4 Product inhibition: remove product continuously
FORMULA REFERENCE
Fed-batch fermentation: add nutrients continuously
Control selectivity: keep CB low to favor desired product
Chemical Engineering Core Concepts
Isothermal Semibatch Reactors

## Slide 93
92 / 114
Non-Isothermal PFR
Energy Balance in Steady-State PFR
Temperature and conversion are coupled in a non-isothermal PFR. Exothermic reactions create hot spots; proper cooling avoids runaway.
1
Hot spot: temperature maximum in exothermic PFR
2
Runaway: if cooling insufficient → T escapes
3
Co-current vs counter-current cooling
4
Adiabatic PFR: U = 0, simplest case
Chemical Engineering Core Concepts
Energy Balance in Steady-State PFR

## Slide 94
93 / 114
CSTR Thermal Design
Energy Balances in Stirred Tank Reactors
Heat generation curve G(T) and heat removal line R(T) are plotted on the same graph. Intersections give possible steady states.
G(T): S-shaped curve for exothermic rxn
R(T): straight line (slope = ṁCp + UA)
Intersections = steady states
Stable SS: G slope < R slope at intersection
FORMULA
G(T) = (−ΔHrxn)·FA₀·X
Chemical Engineering Core Concepts
Energy Balances in Stirred Tank Reactors

## Slide 95
94 / 114
Reactor Stability
Multiple Steady States in Non-Isothermal CSTR
Three intersections of G and R curves give two stable and one unstable steady state. Ignition and extinction can cause abrupt jumps between states.
KEY POINTS
1 Lower SS: stable, low conversion 2 Middle SS: unstable (saddle point) 3 Upper SS: stable, high conversion 4 Light-off temperature: ignition point
FORMULA REFERENCE
Lower SS: stable, low conversion
Middle SS: unstable (saddle point)
Chemical Engineering Core Concepts
Multiple Steady States in Non-Isothermal CSTR

## Slide 96
95 / 114
Fixed Bed Design
Pressure Drop in Packed Bed Reactors
Pressure drop in packed beds affects gas-phase reaction rates via concentration. The Ergun equation combines viscous and inertial contributions.
1
ε ≈ 0.4 for random packed spheres
2
High ΔP → lower concentration → lower rate
3
Modified PFR equation includes P(z)
4
Carman-Kozeny: low Re limit of Ergun
Chemical Engineering Core Concepts
Pressure Drop in Packed Bed Reactors

## Slide 97
96 / 114
Reaction Mechanisms
Steady-State Approximation & Rate-Determining Step
Simplify multi-step rate expressions by assuming intermediates are at steady state (PSSH) or identifying the slowest step as rate-limiting.
PSSH: d[I]/dt = 0 for reactive intermediates
RDS: slowest step controls overall rate
Pre-equilibrium: fast step before RDS
Enzyme kinetics (MM) derived via PSSH
FORMULA
d[I]/dt ≈ 0 (intermediate I)
Chemical Engineering Core Concepts
Steady-State Approximation & Rate-Determining Step

## Slide 98
97 / 114
Biochemical Engineering
Enzyme Kinetics
Enzymes are biological catalysts. The Michaelis-Menten model describes rate as a function of substrate concentration with saturation behavior.
KEY POINTS
1 Km = substrate [S] at V_max/2 2 V_max = k_cat·[E]_total 3 Lineweaver-Burk: 1/v vs 1/[S] linear 4 Competitive inhibitor: increases apparent Km
FORMULA REFERENCE
Km = substrate [S] at V_max/2
V_max = k_cat·[E]_total
Chemical Engineering Core Concepts
Enzyme Kinetics

## Slide 99
98 / 114
Polymer Engineering
Polymerization Kinetics
Step-growth polymerization requires high conversion for high MW. Chain-growth is faster but gives broader molecular weight distributions.
1
Step-growth: all oligomers react equally
2
Chain-growth: initiation → propagation → termination
3
PDI = Mw/Mn ≈ 2 for step-growth at high p
4
Radical chain: PDI ≈ 1.5 (termination by combination)
Chemical Engineering Core Concepts
Polymerization Kinetics

## Slide 100
99 / 114
Numerical Methods
Solving Ordinary Differential Equations
Numerical ODE solvers are essential for non-isothermal reactors, batch reactors, and transient systems where analytical solutions don't exist.
Euler: y_{n+1} = yₙ + h·f(tₙ,yₙ) (simple)
RK4: 4th order accuracy, standard choice
Stiff ODEs: implicit solvers (ode15s, LSODA)
scipy.integrate.solve_ivp (Python)
FORMULA
RK4: k₁=f(t,y), k₂=f(t+h/2,y+hk₁/2)
Chemical Engineering Core Concepts
Solving Ordinary Differential Equations

## Slide 101
100 / 114
Non-Ideal Reactors
Residence Time Distribution
RTD characterizes non-ideal mixing and flow patterns in real reactors by analyzing tracer response curves from pulse or step experiments.
KEY POINTS
1 Ideal PFR: E(t) = δ(t−τ) 2 Ideal CSTR: E(t) = (1/τ)exp(−t/τ) 3 Tanks-in-series: n tanks from E(t) fit 4 Dispersion model: axial mixing parameter
FORMULA REFERENCE
Ideal PFR: E(t) = δ(t−τ)
Ideal CSTR: E(t) = (1/τ)exp(−t/τ)
Chemical Engineering Core Concepts
Residence Time Distribution

## Slide 102
101 / 114
Polymer Production
Polymerization Reactors
Reactor choice affects molecular weight distribution in polymerization. CSTRs give narrow MWD for step-growth; batch gives broader distributions.
1
Step-growth in CSTR: Mw/Mn → 2 (Flory)
2
Chain-growth in CSTR: narrow PDI
3
Semi-batch: control of exotherm
4
PFR for chain-growth: approximates batch
Chemical Engineering Core Concepts
Polymerization Reactors

## Slide 103
102 / 114
Differential Distillation
Single-Stage Batch Distillation
In simple batch distillation (Rayleigh equation), vapor is richer in more volatile component as distillation proceeds and pot composition changes.
More volatile: enriched in early distillate
Pot becomes depleted in light component
Average distillate x̄D < x_D,initial
Limited separation: use reflux for better purity
FORMULA
Rayleigh: ln(L₀/L) = ∫dx/(y*−x)
Chemical Engineering Core Concepts
Single-Stage Batch Distillation

## Slide 104
103 / 114
Batch Columns
Multistage Batch Distillation
Adding stages with reflux greatly improves separation. The minimum reflux ratio gives infinite stages; total reflux gives minimum stages.
KEY POINTS
1 Higher R → better separation, more energy 2 Fenske eq: N_min·ln(α) = ln[(xD(1-xB))/(xB(1-xD))] 3 Underwood equation: R_min from pinch 4 Batch column: product purity varies with time
FORMULA REFERENCE
Higher R → better separation, more energy
Fenske eq: N_min·ln(α) = ln[(xD(1-xB))/(xB(1-xD))]
Chemical Engineering Core Concepts
Multistage Batch Distillation

## Slide 105
104 / 114
Binary Distillation Design
McCabe-Thiele Diagrams
McCabe-Thiele method graphically determines the number of equilibrium stages needed for a binary distillation with a given reflux ratio.
1
Step stages between equilibrium curve & op. lines
2
q-line: feed condition (q=1 saturated liquid)
3
Pinch: op. line touches equilibrium curve
4
Optimal feed stage: intersection of op. lines
Chemical Engineering Core Concepts
McCabe-Thiele Diagrams

## Slide 106
105 / 114
Gas-Liquid Operations
Absorption Columns
Absorption column design uses the number of overall gas-phase transfer units (NTU) and height of a transfer unit (HTU) to determine packing height.
HTU = G/(K_ya·A) (packing dependent)
NTU increases with tighter separation
Operating line: above equilibrium curve (absorption)
Flooding velocity sets column diameter
FORMULA
N_OG = ∫(dy)/(y−y*)
Chemical Engineering Core Concepts
Absorption Columns

## Slide 107
106 / 114
Desorption Operations
Stripping Columns
Stripping removes dissolved gases from liquid using steam or inert gas. The operating line lies below the equilibrium curve.
KEY POINTS
1 Operating line: below equilibrium curve 2 S > 1 needed for stripping to be feasible 3 Steam stripping for VOC removal from water 4 Air stripping: aeration for dissolved gases
FORMULA REFERENCE
Operating line: below equilibrium curve
S > 1 needed for stripping to be feasible
Chemical Engineering Core Concepts
Stripping Columns

## Slide 108
107 / 114
Liquid-Liquid Extraction
Hunter-Nash Method for LLE
The Hunter-Nash graphical method uses a ternary phase diagram to step off extraction stages and find minimum solvent ratio.
1
Plot on right-triangle ternary diagram
2
Operating point: intersection of operating lines
3
Step off stages from raffinate to extract
4
Min. solvent: operating point at plait point
Chemical Engineering Core Concepts
Hunter-Nash Method for LLE

## Slide 109
108 / 114
Evaporation Operations
Single-Effect Evaporators
Single-effect evaporators use one kg of steam to evaporate approximately one kg of water — steam economy ≈ 1.
BPE reduces ΔT driving force
Steam economy ≈ 1 (poor efficiency)
Energy balance: steam heat = sensible + latent
LMTD correction for non-isothermal effects
FORMULA
S·λs = L·Cp(T-Tf) + V·λ
Chemical Engineering Core Concepts
Single-Effect Evaporators

## Slide 110
109 / 114
Energy-Efficient Evaporation
Multi-Effect Evaporators
Each effect reuses vapor from the previous effect as heating steam, achieving economy up to n kg evaporated per kg steam consumed.
KEY POINTS
1 Forward feed: feed flows with steam direction 2 Backward feed: counter-current arrangement 3 Economy improves with more effects (capital trade-off) 4 Triple-effect most common in industry
FORMULA REFERENCE
Forward feed: feed flows with steam direction
Backward feed: counter-current arrangement
Chemical Engineering Core Concepts
Multi-Effect Evaporators

## Slide 111
110 / 114
Transient Heat Transfer
Lumped Capacitance Transient Conduction
When Bi < 0.1, spatial temperature gradients within a solid are negligible — the lumped capacitance model gives exponential cooling/heating.
1
Bi = hLc/k < 0.1 (required condition)
2
Lc = V/As (characteristic length)
3
τ small: fast response (thin, conductive objects)
4
Applications: quenching, thermometry, food cooling
Chemical Engineering Core Concepts
Lumped Capacitance Transient Conduction

## Slide 112
111 / 114
Heat Transfer
Transient Conduction in Sphere with Spatial Effects
For large Biot numbers, temperature varies with position inside a sphere. Heisler charts or one-term Fourier series provide solutions.
Fo > 0.2: one-term approximation valid
Heisler charts: T_center and average T
C₁, ζ₁: tabulated vs. Bi
α = k/(ρCp) = thermal diffusivity [m²/s]
FORMULA
Fo = αt/r₀² (Fourier number)
Chemical Engineering Core Concepts
Transient Conduction in Sphere with Spatial Effect

## Slide 113
112 / 114
Short-Time Heat Transfer
Transient Conduction into Semi-Infinite Solid
Sudden surface temperature change creates a temperature wave that penetrates into a semi-infinite solid via the error function solution.
KEY POINTS
1 erfc = 1 − erf (complementary error function) 2 Penetration depth: T change felt at distance 4√(αt) 3 α large (metals) → fast penetration 4 Applications: welding, fire safety analysis, casting
FORMULA REFERENCE
erfc = 1 − erf (complementary error function)
Penetration depth: T change felt at distance 4√(αt)
Chemical Engineering Core Concepts
Transient Conduction into Semi-Infinite Solid

## Slide 114
113 / 114
External Forced Convection
Convective Heat Transfer over a Flat Plate
Forced convection over a flat plate is solved using boundary layer theory. Nusselt number correlations give the heat transfer coefficient.
1
Nu = hL/k (dimensionless h)
2
Re_L = U∞·L/ν (plate Reynolds number)
3
Pr = ν/α = Cp·μ/k (Prandtl number)
4
Turbulent: Nu = 0.037·Re^0.8·Pr^(1/3)
Chemical Engineering Core Concepts
Convective Heat Transfer over a Flat Plate

## Slide 115
114 / 114
Natural Convection
Free Convection
Natural convection is driven by buoyancy from density differences due to temperature gradients. Rayleigh number governs the heat transfer rate.
β = volumetric thermal expansion coeff.
Ra < 10⁹: laminar; Ra > 10⁹: turbulent
C and n from Churchill-Chu correlation
Applications: cooling fins, building heat loss, electronics
FORMULA
Ra = Gr·Pr = gβΔTL³/(να)
Chemical Engineering Core Concepts
Free Convection