## Slide 1
MEMORY PALACE
Chemical Engineering
Object → Concept → Equation → Recall
114
Concepts
114
Objects
9
Subjects
Each slide: Object image + labeled visual metaphor + ONE key equation

## Slide 2
1
Iterative Solutions
🎮 Table
xₙ+₁ = xₙ − f(xₙ) / f'(xₙ) [Newton-Raphson]
💡 TABLE adjusts its legs (iterations) until perfectly level (residual → 0)
Leg 1 = iteration 1
Each table leg adjustment is
one N-R iteration step
Leg 2 = iteration 2
Refine root estimate
with each step
Flat top = converged!
Stable table = |xₙ+₁ − xₙ| < ε
Residual reached zero

## Slide 3
2
Manometry
🛁 Bathtub
ΔP = ρ·g·h
💡 BATHTUB tilted → water shifts sides → height difference × ρg = pressure difference
Water level LEFT = P₁
One side of the U-tube
manometer at pressure P₁
Water level RIGHT = P₂
Other side balanced
at pressure P₂
Height diff h
The column height
difference gives ΔP = ρgh
Dense fluid sinks ↓
Like soap settling at
bath bottom

## Slide 4
3
Material Balances
💡 Lamp
Accumulation = In − Out + Gen − Consumption
💡 LAMP: electricity IN = light + heat OUT. Nothing disappears. Atoms in = atoms out.
Electricity IN →
Feed streams entering
the system boundary
← Light OUT
Product streams exiting
the system
← Heat OUT
Waste/byproduct
streams leaving
Shade = boundary
System boundary: only
count flows crossing it

## Slide 5
4
Degrees of Freedom
🚪 Door
DOF = Unknowns − Independent Equations
💡 DOOR has 1 DOF (open angle). Add a lock (constraint) → DOF = 0, fully determined.
Hinge = 1 DOF
One degree of motion
(angle of opening)
Lock = constraint (−1)
Each equation/spec
removes one DOF
DOF = 0 → solvable!
Exactly specified: unique
solution exists
DOF > 0 → under-specified
DOF < 0 → over-specified
Check DOF BEFORE solving!

## Slide 6
5
Recycle Mass Balances
🗑 Trash Can
Overall: F = D + B | Recycle ratio R = recycle/product
💡 TRASH CAN: scraps returned to cooking = recycle stream! Overall balance first, then units.
Feed F →
Fresh feed entering
the process
Product D →
Desired product
leaving the system
Waste → recycle back
Unconverted material
returned to reactor inlet

## Slide 7
6
Chemical Reactions
🫙 Blender
ξ = (nₐ − nₐ₀) / (−a) | nᵢ = nᵢ₀ + νᵢ·ξ
💡 BLENDER mixes reactants → blades (reaction) → products. Can't get more smoothie than fruits!
Fruits IN = reactants
Initial moles nᵢ₀
fed into reactor
Blades = reaction
Stoichiometric conversion
via balanced equation
Smoothie = products
Final moles calculated
from extent ξ
Limiting = least fruit
Smallest nᵢ₀/|νᵢ|
determines max ξ

## Slide 8
7
Reactive Material Balances
☕ Coffee Maker
nᵢ,ₒᵤₜ = nᵢ,ᵢₙ + νᵢ · ξ
💡 COFFEE MAKER: water + grounds → extraction reaction → coffee. Atoms always conserved.
Water + grounds IN
Molecular species
entering the reactor
Extraction = reaction
Extent ξ tracks how
far reaction proceeds
Coffee OUT
Product species: molecular
form changed, atoms conserved

## Slide 9
8
Purge Stream in Recycle
🪣 Sink Cabinet
F · yᵢ = P · yᵢ,ₚᵤᵣgₑ (inert balance at steady state)
💡 SINK CABINET: gunk builds up under the sink → drain (purge) removes it to prevent overflow.
Gunk = inerts accumulate
Without purge, inerts build
up in recycle loop indefinitely
Drain = PURGE stream
Bleeds off accumulated
inerts to reach steady state
Feed inerts in
Inerts enter with fresh
feed at mole fraction yᵢ

## Slide 10
9
Transient Material Balances
🗿 Sculpture
dM/dt = ṁᵢₙ − ṁₒᵤₜ
💡 SCULPTURE being carved: shape changes over time (transient). Finished statue = steady state.
Chisel = ṁ in/out
Mass flow rates adding
or removing material
Shape changing = dM/dt ≠= 0
Accumulation term is
non-zero: ODE in time
Finished = dM/dt → 0
Steady state reached when
accumulation vanishes

## Slide 11
10
Wet and Dry Basis
🚿 Sink Top
yᵢ,wₑₜ = yᵢ,dᵣy / (1 + moisture fraction)
💡 SINK TOP: wet surface = wet basis (water included). Wipe dry → only solids left = dry basis.
Wet surface = WET basis
Composition includes
all water content
Wipe dry → DRY basis
Composition on water-free
basis (solids only)

## Slide 12
11
Combustion Reactions
🔥 Stove Top
CₓHᵧ + (x+y/4)O₂ → xCO₂ + (y/2)H₂O
💡 STOVE TOP burns gas: too little O₂ → CO (incomplete). Too much air → dilute & cool.
Fuel (CH₄) IN
Hydrocarbon fuel
entering combustion zone
Flame = combustion
Rapid exothermic oxidation
of fuel with oxygen
CO₂ + H₂O OUT
Complete combustion
products (flue gas)
% Excess Air
(Airₐctual − Airₛtoich) / Airₛtoich × 100

## Slide 13
12
Ideal Gas Law
💨 Range Hood
PV = nRT (R = 8.314 J/mol·K)
💡 RANGE HOOD: hot cooking gases rise (high T → high V). Hood removes them — PV = nRT governs!
Hot gas rises (↑T → ↑V)
Temperature increase causes
volume expansion at const P
Hood sucks gas out
Removes expanded hot
gases from kitchen
STP: 1 mol = 22.4 L
Ideal: no forces, point particles
Valid: low P, high T

## Slide 14
13
Equations of State
🗿 Sculpture
(P + a/v²)(v − b) = RT [van der Waals]
💡 SCULPTURE is REAL — actual volume (b) and surface attraction (a). Ideal gas = featureless ghost.
Real volume → b
Parameter b: excluded volume
from finite molecular size
Surface attraction → a
Parameter a: intermolecular
attractive forces (a/v²)
Z = Pv/RT
Compressibility factor:
Z=1 ideal, Z≠=1 real

## Slide 15
14
Lever Rule
🪟 Glass Wall
V/(L+V) = (xₒᵥₑᵣₐₗₗ − xₗᵢq) / (xᵥₐₚ − xₗᵢq)
💡 GLASS WALL: look left (liquid) and right (vapor). Seesaw — distance to each phase = fraction.
LEFT = liquid (xₗᵢq)
Liquid-phase composition
on the tie line
RIGHT = vapor (xᵥₐₚ)
Vapor-phase composition
on the tie line
YOU = overall comp.
Your position on the seesaw
determines phase fractions

## Slide 16
15
Phase Equilibrium
🪑 Bench
Gibbs Phase Rule: F = C − P + 2
💡 BENCH: sit (liquid), stand (gas), lie flat (solid). Triple point = all 3 simultaneously at one T,P.
Sit = LIQUID
One phase state: molecules
closely packed, fluid
Stand = GAS
Low density, fills container
high kinetic energy
Lie = SOLID
Fixed lattice structure
lowest energy state
Triple pt: F = 0 (3 phases, 1 comp)
Critical pt: ∂ P/∂ V = 0, ∂ ² P/∂ V ² = 0

## Slide 17
16
Clausius-Clapeyron & Antoine
📺 Screen
ln(P₂/P₁) = ΔHᵥₐₚ/R · (1/T₁ − 1/T₂)
💡 SCREEN displays the vapor pressure vs T curve — exponential rise. Antoine gives 3-parameter precision.
Curve on screen = P* vs T
Vapor pressure increases
exponentially with T
Slope = ΔHᵥₐₚ
Heat of vaporization
drives the P-T relationship
Antoine: log ₁₀ (P*) = A − B / (C + T)
Clapeyron: dP / dT = ΔH / (T · Δv)

## Slide 18
17
Raoult's Law and VLE
🔊 Speaker Sub
pᵢ = xᵢ · Pᵢ* | yᵢ = pᵢ / Pₜₒₜₐₗ
💡 SPEAKER blends sound channels. Raoult: each component contributes xᵢ × Pᵢ* to total pressure.
Channel 1 = comp. 1
Component 1 contributes
partial pressure x₁·P₁*
Channel 2 = comp. 2
Component 2 contributes
partial pressure x₂·P₂*
Mixed sound = Pₜₒₜₐₗ
Total P = sum of all
partial pressures (Dalton)
Bubble P: P = Σxᵢ · Pᵢ*
Dew P: 1/P = Σyᵢ / Pᵢ*

## Slide 19
18
Colligative Properties
🍽 Stacked Plates
ΔTb = Kb·m | ΔTf = Kf·m | π = MRT
💡 Each PLATE added (mole of solute) raises boiling point. More plates = more colligative effect!
Each plate = 1 mol solute
Colligative: depends only
on number of particles
More plates → ↑Tb
Boiling point elevation
proportional to molality m
Osmotic π = MRT
Osmotic pressure from
dilute solution theory

## Slide 20
19
Ternary Phase Diagrams
🔧 Oven Grate
xₐ + xᵦ + x꜀ = 1 (triangle vertices = pure components)
💡 OVEN GRATE: three bars, three components. Each junction on triangular grid = ternary mixture.
Vertex A = pure A
Each triangle corner
represents 100% of one comp.
Vertex C = pure C
Interior points are
mixtures of all three
Tie line = 2 phases
Connects equilibrium
compositions of two phases

## Slide 21
20
Psychrometric Chart
🚽 Toilet
ω = 0.622·Pw/(P−Pw) | φ = Pw/Pₛₐₜ(T)
💡 TOILET in bathroom: moisture everywhere. Condensation on bowl = dew point reached!
Moisture = humidity ω
Humidity ratio: kg water
per kg dry air
Bowl condensation = dew pt
Temperature at which
φ reaches 100%
φ = Pw/Pₛₐₜ
Relative humidity: actual
vs saturation vapor pressure

## Slide 22
21
Adsorption
🪞 Wall Mirror
Langmuir: q = qₘₐₓ·KC / (1 + KC)
💡 MIRROR surface collects dust (adsorbate) on glass (adsorbent). Wipe off = desorption.
Glass = adsorbent
Solid surface with
finite adsorption sites
Dust = adsorbate
Gas/liquid molecules
adhering to surface
Finite sites → qₘₐₓ
Monolayer saturation:
all sites occupied
Freundlich: q = K·C¹/ⁿ
BET: multilayer adsorption

## Slide 23
22
State Functions
♟ Chess Board
State: U, H, S, G, V | Path: q, w
💡 CHESS: king's position = state function (doesn't matter which moves got it there).
Position = STATE
U, H, S, G, V depend only
on current T, P, composition
Moves = PATH (q, w)
Heat q and work w depend
on the process path taken
Hess's Law: ΔH path-free
Enthalpy change same
regardless of route

## Slide 24
23
Steam Tables
⌨️ Keyboard
H = Hf + x·Hfg | x = (H − Hf) / Hfg
💡 KEYBOARD lookup: press T or P key → get H, S, v. Steam tables = the keyboard of thermo.
Press T key → get H
Input temperature to find
enthalpy from sat. tables
Press P key → get S
Input pressure for
entropy, specific volume
Quality x = vapor frac.
x = fraction vapor in
two-phase region (0→1)

## Slide 25
24
Mechanical Energy Balance
⚙️ Mech Device
ΔP/ρ + Δ(v²)/2 + g·Δz + F = Wₛ
💡 MECHANICAL device: pump adds energy, turbine extracts. Extended Bernoulli + friction + shaft work.
Pressure ΔP/ρ
Pressure energy per
unit mass of fluid
Kinetic Δv²/2
Change in kinetic energy
due to velocity change
Potential gΔz
Elevation change
gravitational PE
Friction F (Darcy)
Frictional losses from
Darcy-Weisbach: f·L/D·v²/2

## Slide 26
25
Heat Capacities
💡 Table Lamp
Q = n·Cₚ·ΔT | Cₚ − Cᵥ = R (ideal gas)
💡 TABLE LAMP heats up: Q = nCₚΔT joules. Cₚ > Cᵥ because constant-P allows expansion work.
Touch → hot! Q = nCₚΔT
Heat needed to raise T
at constant pressure
γ = Cₚ/Cᵥ
Heat capacity ratio
for isentropic processes
Cₚ polynomial: a + bT + cT²
Shomate equation fits
Cₚ vs T data

## Slide 27
26
Energy Balance + Phase Change
✨ Glow
Qₜₒₜₐₗ = Qₛₑₙₛᵢbₗₑ + Qₗₐₜₑₙₜ = ∫Cₚ dT + ΣΔHₚₕₐₛₑ
💡 GLOWING: add heat → T rises (sensible), then GLOWS at transition (latent heat, isothermal).
Heat → T rises (sensible)
Temperature increases while
phase remains the same
GLOW = phase change
Latent heat absorbed at
constant T during transition
ΔHᵥₐₚ, ΔHfᵤₛ
Enthalpies of vaporization
and fusion respectively

## Slide 28
27
Flash Separations
💡 Ceiling Lamp
Σ zᵢ(Kᵢ−1) / (1 + V/F·(Kᵢ−1)) = 0 [Rachford-Rice]
💡 CEILING LAMP illuminates two phases below: vapor rises UP (light), liquid falls DOWN (heavy).
Vapor rises ↑ (light)
More volatile components
enriched in vapor phase
Liquid falls ↓ (heavy)
Less volatile components
concentrate in liquid
Kᵢ = yᵢ/xᵢ
Equilibrium ratio: volatility
of each component (Raoult: Pᵢ*/P)

## Slide 29
28
Heats of Reaction
🔦 Floor Lamp
ΔH°ᵣₓₙ = Σνᵢ·ΔH°f,ₚᵣₒd − Σνᵢ·ΔH°f,ᵣₑₐcₜ
💡 FLOOR LAMP: plug in reactants → energy released as light (exothermic, −ΔH). Hess's Law!
Plug in = reactants
Starting materials with
known heats of formation
Light out = −ΔH (exo)
Negative ΔH releases
energy to surroundings
+ΔH = endothermic
Positive ΔH absorbs
energy from surroundings

## Slide 30
29
Energy Balance + Reaction
🔆 Lamp Shade
Q = ΔHᵣₓₙ · ξ + ΔHₛₑₙₛᵢbₗₑ
💡 SHADE controls how much heat/light escapes the reactor. Balances generation vs removal.
Shade = heat exchanger
Controls heat transfer
between reactor and surroundings
Light = ΔHᵣₓₙ·ξ
Heat generated/consumed
proportional to extent ξ
Adiabatic: Q=0
No heat exchange: all
rxn heat stays in system

## Slide 31
30
Adiabatic Flame Temperature
🕯 Table Lamp
ΔHᵣₓₙ + ∫(Tᵣₑf → Tₐd) n·Cₚ dT = 0 (Q = 0)
💡 LAMP sealed in insulating box: all energy → heat → maximum temperature Tₐd.
Sealed box = adiabatic
No heat escapes:
perfect insulation (Q=0)
Max T = Tadiabatic
Highest possible flame T
achieved with zero heat loss
Less excess air → higher Tad
Extra air dilutes products
and absorbs heat → lower T

## Slide 32
31
1st Law – Closed Systems
🍷 Wine Bottle
ΔU = Q − W
💡 WINE BOTTLE sealed (closed system). Heat wine (Q) → expands → cork pops (W = P·ΔV).
Sealed = closed system
No mass crosses the
system boundary
Heat Q in →
Energy added as heat
(positive Q into system)
Cork pops = W out
Boundary work done by
system: W = ∫P dV
ΔU stored internally
Whatever isn't work
changes internal energy

## Slide 33
32
Buoyancy
🥂 Wine Glass
Fb = ρfₗᵤᵢd · g · Vₛᵤbₘₑᵣgₑd
💡 WINE GLASS in water: does it float? ρgₗₐₛₛ > ρwₐₜₑᵣ → sinks! Archimedes' principle.
Buoyant force ↑
Upward force = weight of
displaced fluid volume
Weight ↓
Gravity pulling object
downward by its mass
Float if ρobj < ρfluid
Object less dense than fluid
will be buoyed upward

## Slide 34
33
Properties of Fluids
🥃 White Wine Glass
μ = τ / (du/dy) | ν = μ/ρ | σ = F/L
💡 WHITE WINE pours easily (low μ). Oil is thick (high μ). Meniscus in glass = surface tension σ.
Pour → viscosity μ
Dynamic viscosity: resistance
to shear deformation (Pa·s)
Meniscus = σ
Surface tension: force per
unit length at interface (N/m)
ρ = m/V
Density: mass per unit
volume (kg/m³)

## Slide 35
34
Hydrostatic Pressure
🍷 Wine Glass
P = P₀ + ρ·g·h
💡 WINE GLASS: pressure at bottom > top. Deeper wine = more weight pressing down = higher P.
Top: P₀ (atmospheric)
Surface exposed to
atmospheric pressure
Bottom: P₀ + ρgh
Pressure increases linearly
with depth h
h = depth ↓
Measured downward from
free surface

## Slide 36
35
Submerged Gates
🚪 Door (underwater)
Fᵣ = ρg·ȳ·A | ycₚ = ȳ + Iɢ/(ȳ·A)
💡 UNDERWATER DOOR: water pushes harder at bottom. Center of pressure always below centroid.
Force Fᵣ = ρg·ȳ·A
Resultant hydrostatic force
on the submerged surface
Centroid ȳ
Depth of geometric center
of the submerged area
Center of pressure ycₚ ↓
Point where resultant acts:
always below centroid

## Slide 37
36
Bernoulli's Equation
🚿 Shower Head
P + ½ρv² + ρgz = constant
💡 SHOWER HEAD: narrow holes → fast stream (↑v, ↓P by Bernoulli). Wide pipe = slow, high P.
Wide pipe: slow, high P
Large cross-section: low velocity
high static pressure
Narrow nozzle: fast, low P
Constriction accelerates flow:
venturi effect drops pressure
P + ½ρv² + ρgz = const
Energy conservation along
a streamline (inviscid, steady)

## Slide 38
37
Viscosity & Shear Stress
🔧 Shower Handle
τ = μ · (du/dy)
💡 SHOWER HANDLE: twist = shear stress τ. Hard to turn (honey) = high μ. Easy (water) = low μ.
Twist = shear stress τ
Force per unit area
parallel to surface
Resistance = viscosity μ
Newton's law: proportionality
constant between τ and du/dy
Re = ρvD/μ
Reynolds number: ratio
of inertial to viscous forces

## Slide 39
38
Conservation of Mass
🗄 Wall Cabinet
ρ₁A₁v₁ = ρ₂A₂v₂ (incompressible: A₁v₁ = A₂v₂)
💡 WALL CABINET: nothing appears or disappears inside. What goes in must come out!
IN: ρ₁A₁v₁
Mass flow rate entering:
density × area × velocity
OUT: ρ₂A₂v₂
Mass flow rate leaving:
must equal inlet at SS
Area ↓ → velocity ↑
Continuity: pipe narrows
→ flow speeds up

## Slide 40
39
Intro to Pipe Flow
🚿 Faucet
Re = ρvD/μ | Laminar: Re<2100 | Turbulent: Re>4000
💡 FAUCET: low flow = smooth laminar stream. Full blast = splashing turbulent chaos!
Gentle = LAMINAR
Re < 2100: smooth ordered
layers, predictable flow
Full blast = TURBULENT
Re > 4000: chaotic mixing
eddies, enhanced transport
Re = ρvD/μ
Dimensionless ratio:
inertial forces / viscous forces

## Slide 41
40
Velocity Profiles in Pipe
🚰 Faucet
Laminar: v(r) = vₘₐₓ(1−(r/R)²) | vₐᵥg = vₘₐₓ/2
💡 FAUCET: center flows fastest, zero at wall (no-slip). Parabolic profile = laminar.
Center = fastest vₘₐₓ
Maximum velocity at the
centerline of the pipe
Wall = zero (no-slip)
Fluid sticks to pipe wall:
v = 0 at r = R
Parabolic profile
Laminar: parabola shape
Turbulent: flatter (1/7 law)

## Slide 42
41
Boundary Layer
🧻 TP Holder
δ = 5x/√Reₓ (laminar) | Transition: Reₓ ≈ 5×10⁵
💡 TOILET PAPER unrolling: boundary layer builds as you pull. Near pin = thin δ, further = thick.
Pin = leading edge
δ starts at zero at
the leading edge
Further → δ grows
BL thickness increases
with distance downstream
No-slip at wall: v=0
Velocity goes from 0 at
surface to U∞ at edge of δ

## Slide 43
42
Entrance Length
🗑 Hamper Flap
Lₑ/D = 0.06·Re (laminar) | Lₑ/D ≈ 4.4·Re¹/⁶ (turb.)
💡 HAMPER FLAP: open it → flow chaotic near entry. After Lₑ distance, settles into final pattern.
Entry = developing
Velocity profile changing
with position x
After Lₑ = fully developed
Profile no longer changes:
correlations valid beyond Lₑ

## Slide 44
43
Pressure Drop in Pipes
🥛 Toothbrush Cup
ΔP = f·(L/D)·(ρv²/2) [Darcy-Weisbach]
💡 TOOTHBRUSH CUP: fill by pumping water up pipe. Friction wastes energy — Darcy-Weisbach calculates it.
f = friction factor
From Moody chart: f(Re, ε/D)
Laminar: f = 64/Re
L/D = pipe geometry
Longer pipe / smaller diameter
= more friction loss
Power = Q·ΔP/η
Pump power required to
overcome frictional losses

## Slide 45
44
Equivalent Length
💡 Bedroom Lamp
Lₑq = K·D/f | ΔPₜₒₜₐₗ = f·(L + ΣLₑq)/D · (ρv²/2)
💡 BEDROOM LAMP with extension cord: cord adds resistance. Each valve/elbow = extra cord length.
Direct wire = pipe L
Straight pipe contributes
friction over length L
Extension cord = Lₑq
Fittings expressed as
equivalent extra pipe length
K = loss coefficient
Tabulated for each fitting:
valve, elbow, tee, etc.

## Slide 46
45
Multipipe Systems
🗄 Bedroom Cabinet
Series: Q same, ΔP = ΣΔPᵢ | Parallel: ΔP same, Q = ΣQᵢ
💡 CABINET: drawers side-by-side (parallel, same ΔP) or stacked (series, same Q).
Side-by-side = PARALLEL
Same pressure drop across
each branch; flows add up
Stacked = SERIES
Same flow through each;
pressure drops add up

## Slide 47
46
Linear Momentum
🔊 Speaker Sub
ΣF = ṁ(vₒᵤₜ − vᵢₙ)
💡 SPEAKER CONE pushes air (momentum transfer). Force on cone = rate of change of air momentum.
Cone push = force F
External forces: pressure,
gravity, wall reactions
Air pushed = ṁ·Δv
Momentum flux change
across control volume
Pipe bends, nozzles
Direction change creates
forces on pipe supports

## Slide 48
47
Pressure Field at Rest
🛏 Pillow
∇P = ρg (Navier-Stokes at rest: v=0 → all velocity terms vanish)
💡 PILLOW at rest: no motion, just gravity pressing down. N-S simplifies to ∇P = ρg.
No motion → v=0
Static fluid: all velocity
and acceleration terms vanish
Gravity only → ∇P = ρg
Pressure gradient equals
fluid weight per unit volume

## Slide 49
48
Velocity Profiles (N-S)
🗄 Closet Dresser
Couette: u = U·y/H | Poiseuille: u = (R²−r²)/(4μ)·(−dP/dx)
💡 CLOSET DRESSER: clothes organized in layers = organized laminar flow layers from wall to center.
Bottom drawer = wall (v=0)
No-slip boundary condition:
fluid stationary at wall
Top drawer = fastest
Maximum velocity at
centerline or moving plate
Parabolic = Poiseuille
Pressure-driven pipe flow
with parabolic velocity profile

## Slide 50
49
Dimensional Analysis
🪞 Mirror
Π groups = n − k | Re = ρvL/μ | Nu = hL/k
💡 MIRROR reflects: dimensionless numbers reflect physical similarity between different flows.
Re = inertia/viscous
Reynolds number: determines
laminar vs turbulent regime
Fr = inertia/gravity
Froude number: important
for free-surface flows
Nu = conv/cond heat
Nusselt: ratio of convective
to conductive heat transfer

## Slide 51
50
Modeling & Similitude
🗃 Apt Dresser
Reₘₒdₑₗ = Reₚᵣₒₜₒₜyₚₑ or Frₘₒdₑₗ = Frₚᵣₒₜₒₜyₚₑ
💡 DRESSER = scale model of a room. Match Re (viscous) or Fr (free-surface) for similarity.
Mini furniture = model
Small-scale replica built
for testing in lab
Match Re or Fr
Dynamic similarity: match
the dominant dimensionless group
Geometric: Lₘ/Lₚ = λ
All lengths scaled by
the same factor λ

## Slide 52
51
1st Law Closed (Processes)
🪑 End Table
Isothermal: Q = W = nRT·ln(V₂/V₁) | Adiabatic: Q = 0, ΔU = −W
💡 END TABLE: fixed contents, closed top. Heat (Q) → stores (ΔU) or does work (W).
Const T: ΔU=0
Isothermal ideal gas:
all heat becomes work
Const V: W=0
Isochoric: no volume change
so no boundary work
Adiabatic: Q=0
Insulated: internal energy
changes only via work

## Slide 53
52
1st Law – Open Systems
☕ End Table
Q̇ − Ẇₛ = ṁ[Δh + Δv²/2 + gΔz]
💡 END TABLE in café: cups come and go (open system). H = U + PV includes flow work.
Cups IN = ṁᵢₙ · hᵢₙ
Enthalpy carried in by
mass flow streams
Cups OUT = ṁₒᵤₜ · hₒᵤₜ
Enthalpy leaving with
exit mass flows
H = U + PV (enthalpy)
Accounts for both internal
energy and flow work

## Slide 54
53
Unsteady Energy on Tanks
🪑 Bench
d(mU)/dt = Q̇ − Ẇ + ṁᵢₙ·hᵢₙ − ṁₒᵤₜ·hₒᵤₜ
💡 BENCH loaded over time: weight (internal energy) increases. Unsteady = load changes with t.
Loading = ṁᵢₙ·hᵢₙ
Energy input from
incoming mass flows
d(mU)/dt ≠ 0
Accumulation term is non-zero:
transient energy balance ODE

## Slide 55
54
Entropy
📺 TV
dS = δQᵣₑᵥ/T | ΔSᵤₙᵢᵥₑᵣₛₑ ≥ 0 (2nd Law)
💡 TV: scrambled signal = high entropy. Clear picture = low S. Signals get noisier (ΔS↑ always).
Clear signal = low S
Ordered state: fewer
microstates, low entropy
Static noise = high S
Disordered state: many
microstates, high entropy
ΔSᵤₙᵢᵥ ≥ 0 always
Second Law: universe entropy
never decreases

## Slide 56
55
Turbines & Compressors
🎮 Game Controller
ηₜᵤᵣb = (h₁−h₂)/(h₁−h₂ₛ) | ηcₒₘₚ = (h₂ₛ−h₁)/(h₂−h₁)
💡 CONTROLLER: turbine = output (joystick pushes out power). Compressor = input (buttons pressed in).
Joystick OUT = turbine
Extracts shaft work from
high-pressure fluid
Buttons IN = compressor
Adds shaft work to
increase fluid pressure
η < 1 (irreversibility)
Isentropic efficiency accounts
for real-world friction/heat losses

## Slide 57
56
Rev. & Irrev. Expansion
💻 Computer Table
Wᵣₑᵥ = nRT·ln(V₂/V₁) (isothermal) | Wᵢᵣᵣₑᵥ = Pₑₓₜ·ΔV
💡 NEAT DESK = reversible (max efficiency). MESSY DESK = irreversible (wasted effort).
Neat = reversible
Maximum work extracted
or minimum work input
Messy = irreversible
Less work out, more in;
entropy generated
Wᵣₑᵥ > Wᵢᵣᵣₑᵥ (exp.)
Reversible expansion always
yields more useful work

## Slide 58
57
Isentropic Process
🖱 Computer Mouse
PVγ = const | T₂/T₁ = (P₂/P₁)⁽ˠ⁻¹⁾/ˠ
💡 MOUSE: smooth frictionless glide = reversible + adiabatic = isentropic. Drag = entropy.
Smooth glide = isentropic
No friction, no heat loss:
entropy constant (ΔS=0)
Friction = irreversible
Real processes generate
entropy from dissipation
γ = Cₚ/Cᵥ
Heat capacity ratio:
always > 1 for real gases

## Slide 59
58
Carnot Cycle
🪟 Window Frame
η꜀ₐᵣₙₒₜ = 1 − Tₗ/Tʜ
💡 WINDOW: hot inside (Tʜ), cold outside (Tₗ). Carnot extracts work from ΔT. No engine beats it!
Inside = Tʜ (hot)
High-temperature thermal
reservoir (heat source)
Outside = Tₗ (cold)
Low-temperature sink
(heat rejection)
Bigger ΔT → more η
Maximum theoretical efficiency
for any heat engine
COPʜₚ = Tʜ / (Tʜ−Tₗ)
COPᵣₑf = Tₗ / (Tʜ−Tₗ)

## Slide 60
59
Rankine Cycle
🏺 Vase
η = (Wₜᵤᵣbᵢₙₑ − Wₚᵤₘₚ) / Qbₒᵢₗₑᵣ
💡 VASE: fill water (pump) → heat (boiler) → steam pushes (turbine) → condense → repeat.
Fill = pump
Liquid water pressurized
with minimal work input
Heat = boiler
Heat added at high P:
liquid → superheated steam
Steam → turbine
Steam expands through turbine
extracting shaft work
Cool back = condenser
Vapor condensed back to
liquid, rejecting heat to sink

## Slide 61
60
Refrigeration Cycle
❄️ Fridge
COP = Qₗ / Ẇcₒₘₚ = (h₁−h₄) / (h₂−h₁)
💡 FRIDGE: cold inside (evaporator absorbs Qₗ), hot back (condenser rejects Qʜ). COP > 1!
Inside cold = evaporator
Refrigerant absorbs heat Qₗ
at low T inside the fridge
Back hot = condenser
Rejects heat Qʜ to kitchen
at high T behind fridge
COP > 1 possible!
Unlike efficiency, COP can
exceed unity (not % limited)

## Slide 62
61
Throttling (Joule-Thomson)
🪞 Mirror Plate
h₁ = h₂ (isenthalpic) | μJₜ = (∂T/∂P)ʜ
💡 MIRROR reflects same enthalpy (h₁=h₂), but pressure and temperature redistribute through valve.
Same H reflected
Isenthalpic: enthalpy unchanged
across throttle valve
P drops, T may drop
Irreversible expansion:
no work extracted
μJₜ > 0 → cools
Positive J-T coefficient:
gas cools on expansion (for refrig.)

## Slide 63
62
Fundamental Relations
🗄 Wall Cabinet
dU = TdS − PdV | dH = TdS + VdP | dA = − SdT − PdV | dG = − SdT + VdP
💡 CABINET: 4 drawers (U,H,A,G), each opens with 2 keys (natural variables). Maxwell = diagonals.
Drawer U: keys S,V
Internal energy: natural
variables are entropy & volume
Drawer H: keys S,P
Enthalpy: natural variables
are entropy & pressure
Drawer G: keys T,P
Gibbs energy: most useful
at constant T,P (lab conditions)
Drawer A: keys T,V
Helmholtz energy: useful
for constant T,V systems

## Slide 64
63
Liquefaction
🗄 Storage Cabinet
y (liq. fraction) = (h₂ − h₁) / (h₂ − hf)
💡 CABINET stores liquefied gas. Gas squeezed through door crack (throttle) → cools → liquefies.
Gas in (warm)
High-pressure gas enters
above inversion temperature
Door crack = throttle
Isenthalpic expansion
cools the gas (J-T effect)
Liquid drips (LN₂, LNG)
Fraction y liquefied;
rest recycled for more cooling

## Slide 65
64
Property Phase Diagrams
🗄 Double-Door Cabinet
PV diagram: area = W | TS diagram: area = Qᵣₑᵥ
💡 DOUBLE DOOR: two panels = two axes (P-V or T-S). Dome shape = two-phase region.
Left door = axis 1
Pressure (PV) or Temperature
(TS) on vertical axis
Right door = axis 2
Volume (PV) or Entropy
(TS) on horizontal axis
Dome = two-phase
Under the dome: liquid-vapor
coexistence region

## Slide 66
65
Departure Functions
🥛 Drinking Glass
H − Hⁱg = RT² ∫(∂Z/∂T)ₚ d(lnP)
💡 GLASS: thick base = departure from thin ideal glass. Real fluid = ideal + departure correction.
Thin ideal = Hⁱg
Ideal gas enthalpy:
no intermolecular interactions
Extra thickness = departure
Correction for real gas:
accounts for molecular forces
Z = Pv/RT
Compressibility factor
measures deviation from ideal

## Slide 67
66
Fugacity
🥛 Drinking Glass
f = φ·P | Phase equil: fₗ = fᵥ
💡 Real liquid escapes with fugacity f, not just vapor pressure. f = corrected pressure for real behavior.
Escaping tendency = f
Fugacity: effective pressure
corrected for non-ideality
f = φ·P
Fugacity coefficient φ from
equation of state
At low P: f → P
Ideal limit: fugacity equals
pressure as P → 0

## Slide 68
67
Partial Molar Quantities
🥣 Bowl
M̄ᵢ = (∂(nM)/∂nᵢ)ₜ,ₚ,ₙⱼ | Mₘᵢₓ = Σxᵢ·M̄ᵢ
💡 BOWL of mixed ingredients: each component contributes M̄ᵢ to total bowl property.
Add 1 spoon salt → ΔV
Partial molar volume: volume
change per mole of i added
M̄ᵢ = partial molar
Contribution of component i
to total mixture property
Gibbs-Duhem: Σxᵢ·dM̄ᵢ=0
Constraint: partial molar
properties not independent

## Slide 69
68
Fugacities of Mixtures
🍽 Plate
f̂ᵢ = yᵢ·φ̂ᵢ·P (vapor) | VLE: f̂ᵢL = f̂ᵢV
💡 PLATE with mixed foods: each item exerts its own escaping tendency (fugacity) in the mixture.
Each food = component
Individual species fugacity
in the mixture phase
φ̂ᵢ from mixture EOS
Fugacity coefficient from PR/SRK
accounts for unlike interactions

## Slide 70
69
Chemical Potential
🥣 Stacked Bowls
μᵢ = (∂G/∂nᵢ)ₜ,ₚ | Equil: μᵢα = μᵢβ
💡 STACKED BOWLS: at equilibrium, liquid level (μ) same in all bowls. High μ → flows to low μ.
Bowl 1 level = μ^α
Chemical potential in phase α:
partial molar Gibbs energy
Bowl 2 level = μβ
Chemical potential in phase β:
must equal μ^α at equilibrium
Equal levels = equil.
Drives mass transfer from
high to low μ until balanced

## Slide 71
70
VLE Non-Ideal (γ)
🗄 Corner Cabinet
P·yᵢ = xᵢ · γᵢ · Pᵢ* [Modified Raoult's]
💡 CORNER CABINET: hard access = non-ideal mixtures deviate from Raoult. γ = angle correction factor.
Straight = ideal (γ=1)
Raoult's Law: ideal solution
no activity coefficient needed
Corner angle = γ ≠ 1
Activity coefficient corrects
for molecular interactions
γ>1: pos. dev. | γ<1: neg.
Margules, Wilson, NRTL
models predict γ values

## Slide 72
71
Osmosis & Reverse Osmosis
🍞 Toaster
π = MRT | RO: apply P > π to push solvent through membrane
💡 TOASTER: push lever (pressure) to force bread (water) through slots (membrane). Push = desalinate!
Lever = applied P
External pressure applied
to overcome osmotic pressure
Slots = membrane
Semipermeable membrane:
only solvent passes through
π = osmotic pressure
Equilibrium pressure from
solute concentration (π=MRT)

## Slide 73
72
Henry's Law & Absorption
💡 Ceiling Lamp
pᵢ = Hᵢ · xᵢ (Henry's Law)
💡 CEILING LAMP: light (gas) shines DOWN into room (liquid). Some light absorbed. Dim lamp = less absorption.
Light above = gas phase
Gas-phase partial pressure
drives dissolution
Room below = liquid
Liquid solvent absorbs
gas at mole fraction xᵢ
High H → low solubility
Large Henry's constant
means gas barely dissolves

## Slide 74
73
Enthalpy of Mixing
🪑 Office Chair
GE = RT · Σxᵢ · ln(γᵢ) | ΔHₘᵢₓ = Hₘᵢₓ − Σxᵢ·Hᵢ
💡 MIX two foam types in CHAIR: comfortable (ΔH<0, neg. dev.) or uncomfortable (ΔH>0, pos. dev.).
Good mix → ΔH<0
Exothermic mixing:
strong unlike interactions
Bad mix → ΔH>0
Endothermic mixing:
like-like preferred over unlike

## Slide 75
74
Cubic EOS for VLE
💤 Pillow
PR: P = RT/(v−b) − a(T)/[v(v+b)+b(v−b)]
💡 PILLOW: soft (liquid root) vs fluffy (vapor root). Cubic gives 3 roots; discard unstable middle.
Compressed = liquid root
Smallest volume root:
represents liquid phase
Fluffy = vapor root
Largest volume root:
represents vapor phase
Middle root = unstable
Spinodal region: physically
meaningless, always discard

## Slide 76
75
Gibbs Energy & Phase Sep.
🪵 Table Top
∂²G/∂x² < 0 → unstable → phase separation
💡 TABLE TOP: smooth = stable single phase. Cracked = phase-separated. Common tangent = equilibrium.
Smooth = stable
Concave up Gₘᵢₓ curve:
single-phase thermodynamically stable
Crack = phase separation
Concave down region:
system spontaneously demixes
Spinodal: ∂²G/∂x²=0
Boundary of unstable region;
binodal found by common tangent

## Slide 77
76
Partially Miscible Liquids
🛋 Sofa
At equil: μᵢI = μᵢII | UCST: above → fully miscible
💡 SOFA: two people share but stay in zones (partially miscible). Warm room (↑T) → they can mix.
Person 1 = phase I
Liquid phase α with
composition on binodal
Person 2 = phase II
Liquid phase β with
different binodal composition
Above UCST → mix
Upper critical solution T:
full miscibility above it

## Slide 78
77
Immiscible Liquids
🛋 Main Sofa
P = Pₐ* + Pᵦ* → Boil at T < either pure Tb
💡 Two people who NEVER share space (immiscible). Boil together → both in vapor at lower T.
Never share = immiscible
Zero mutual solubility:
two permanent liquid layers
Steam distillation
Exploit immiscibility to
boil at T lower than either pure

## Slide 79
78
Eutectic Phase Diagrams
🪑 Side Table
Eutectic: 3 phases in equil. (F=0) | Lowest melting composition
💡 SIDE TABLE: solid top (solid) + liquid cups (liquid). Eutectic = composition that melts at lowest T.
Solid top = solid phase
Solidus region below
eutectic horizontal line
Cup = liquid phase
Liquidus region above
the melting curve
Eutectic pt: lowest Tₘ
Invariant point: Pb-Sn solder,
food science applications

## Slide 80
79
Azeotropes
🪟 Window Frame
Azeotrope: xᵢ = yᵢ (can't separate by simple distillation)
💡 WINDOW FRAME: stuck, can't move further. Azeotrope = stuck composition during distillation.
Fixed frame = stuck comp.
Liquid and vapor have
identical compositions
Break: P-swing or entrainer
Change P to shift azeotrope
or add third component
EtOH-H₂O: 95.6%
Classic minimum-boiling
azeotrope at 78.1°C

## Slide 81
80
Gas-Phase Chemical Equil.
🪟 Window
ΔG° = −RT·ln(Kₚ) | Kₚ = Π(Pᵢ/P°)νᵢ
💡 WINDOW: outside = products, inside = reactants. Kₚ tells how far the window opens (→ products).
Inside = reactants
Starting materials at
standard state
Outside = products
Kₚ > 1: products favored
Kₚ < 1: reactants favored
van't Hoff: d(lnK)/dT
ΔH°/(RT²): tells how K
changes with temperature

## Slide 82
81
Heterogeneous Equil.
🪟 Window
Pure solid/liquid: a = 1 → Kₚ = PCO2 (CaCO₃ decomp.)
💡 WINDOW: frame itself is solid (a=1, always there). Only gases appear in Kₚ expression.
Frame = solid (a=1)
Pure solids/liquids: activity
fixed at unity by convention
Outside gas → in Kₚ
Only species with variable
activity appear in K expression
Q vs K: direction
Q < K → forward (make products)
Q > K → reverse (make reactants)

## Slide 83
82
Thermal Effects in Rxns
🛏 Sheet
ln(K₂/K₁) = −ΔH°/R · (1/T₂ − 1/T₁) [van't Hoff]
💡 SHEET: temperature distributed across reactor. van't Hoff shows how K(T) shifts with temperature.
Exothermic: K ↓ with T
Le Chatelier: heating shifts
exo reaction ← backward
Endothermic: K ↑ with T
Heating pushes endo
reaction → forward
Tₐd = T₀ + |ΔH|X/(ΣnCₚ)
Adiabatic temperature rise
from exothermic reaction

## Slide 84
83
Multiple Reaction Equil.
🚪 Door (multi-lock)
Minimize Gₜₒₜₐₗ subject to atom balance constraints
💡 DOOR with multiple locks: each lock = one equilibrium reaction. Must open all simultaneously (ξⱼ).
Lock 1 = rxn 1 equil.
First independent reaction
with its own Kₚ value
Lock 2 = rxn 2 equil.
Second coupled reaction;
extents ξⱼ are coupled
Key set = extents ξⱼ
Gibbs free energy minimization
finds all ξⱼ simultaneously

## Slide 85
84
Nonlinear Regression
🚪 Door (key-fitting)
SSR = Σ(yₒbₛ − yₘₒdₑₗ)² → minimize over parameters
💡 DOOR: try different key shapes (parameters k, α, β) until it fits (minimizes SSR). Right key = data fits!
Wrong key = high SSR
Poor parameter estimates:
large sum of squared residuals
Right key = min SSR
Optimal parameters found
by Levenberg-Marquardt
r = k·Cₐ^α·Cᵦ^β
Power law rate: fit α, β
and pre-exponential k

## Slide 86
85
Multiple Rxns & Selectivity
🚪 Door (multi-keyhole)
Selectivity S = rdₑₛᵢᵣₑd / rᵤₙdₑₛᵢᵣₑd
💡 DOOR with multiple keyholes: insert key carefully to open DESIRED lock only (maximize selectivity S).
Desired lock = target rxn
Rate of desired product
formation rdₑₛᵢᵣₑd
Other locks = side rxns
Undesired parallel/series
reactions consuming feed
PFR favors higher-order
High Cₐ in PFR benefits
higher-order desired reactions

## Slide 87
86
Langmuir-Hinshelwood
🚪 Door (dual-key)
r = k·Kₐ·Cₐ·Kᵦ·Cᵦ / (1 + Kₐ·Cₐ + Kᵦ·Cᵦ)²
💡 DOOR: two keys (A,B) must BOTH be inserted (both adsorb on surface) before door opens (reaction!).
Key A adsorbs → Kₐ
Reactant A adsorbs to
catalyst active site
Key B adsorbs → Kᵦ
Reactant B adsorbs to
adjacent catalyst site
Both in → reaction!
Surface reaction between
two adsorbed species

## Slide 88
87
Thiele Modulus & η
🪑 Chair (foam)
Φ = R√(k/Dₑ) | η = tanh(Φ)/Φ
💡 CHAIR foam cushion: must press through foam (pore diffusion) to reach base (active site). Deep = low η.
Thick foam = high Φ
Large Thiele: reaction fast
relative to diffusion
η << 1 (diffusion limited)
Effectiveness factor low:
interior sites starved of reactant
Small pellet → η ≈ 1
Reduce particle size to
eliminate diffusion limitation

## Slide 89
88
Isothermal Batch Reactor
🪑 Chair (sit & wait)
t = Cₐ₀ ∫dX / (−rₐ)
💡 CHAIR: sit down (load reactants), wait time t for conversion X, stand up (unload). No one enters!
Sit down = load reactants
Charge reactor with initial
concentration Cₐ₀
Wait time t for X
Integrate design equation
to find required batch time
Stand up = unload products
Remove products after
desired conversion achieved

## Slide 90
89
CSTR
🪑 Cafeteria Chair
V = Fₐ₀ · X / (−rₐ)|ₑₓᵢₜ
💡 Cafeteria CHAIR: always occupied, well-mixed. Exit = reactor concentration. Rate at EXIT conditions!
Continuous in/out
Steady flow: feed enters,
product exits continuously
Well-mixed → Cₑₓᵢₜ=Cᵣₑₐcₜₒᵣ
Perfect mixing: composition
uniform throughout tank
Rate at EXIT conditions
rₐ evaluated at exit (low)
concentration → larger V needed

## Slide 91
90
PFR (Plug Flow Reactor)
🪑 Queue Chair
V/Fₐ₀ = ∫₀X dX / (−rₐ)
💡 CHAIR in a queue: first in, first out. Each fluid element waits exactly V/Q time. No mixing, no cutting!
Enter front (inlet)
Feed enters at one end;
concentration highest here
Exit back (outlet)
Products exit after
traveling full reactor length
PFR > CSTR for same X
PFR always smaller volume
for positive-order reactions

## Slide 92
91
Semibatch Reactor
📚 Wall Shelf
dNₐ/dt = Fₐ,ᵢₙ + rₐ · V (variable V)
💡 WALL SHELF: start empty (A inside), add books (B) over time. Controlled addition prevents overload.
A already in reactor
One reactant initially charged
as batch component
Add B slowly over time
Second reactant fed gradually
to control selectivity/temperature
Controls selectivity & heat
Low Cᵦ maintains high
selectivity for desired product

## Slide 93
92
PFR Energy Balance
🪟 Window (PFR view)
dT/dV = [Q̇ − ΔHᵣₓₙ·rₐ] / (Fₐ₀·ΣΘᵢCₚᵢ)
💡 Look through PFR window: T and X change together (coupled ODEs). Hot exothermic PFR fogs the window!
T(z) profile visible
Temperature varies along
reactor length z
Exothermic: T ↑ along L
Risk of hot spot:
runaway if cooling insufficient
Coupled: dX/dV & dT/dV
Solve simultaneously with
numerical ODE solver (RK4)

## Slide 94
93
CSTR Energy Balance
🪟 Window (CSTR)
G(T) = R(T) [heat generation = heat removal at SS]
💡 Heat generated G (S-curve) vs heat removed R (line). Intersections = steady state(s)!
G(T) = heat generation
S-shaped curve from Arrhenius
temperature dependence of rate
R(T) = heat removal
Linear: ṁCₚ(T−T₀)
+ UA(T−Tₐ) from cooling
Intersection = SS
Where G=R: possible
multiple intersections

## Slide 95
94
Multiple Steady States
💡 Wall Lamp
dG/dT > dR/dT → unstable | Ignition & extinction points
💡 WALL LAMP: ON (high-T SS) or OFF (low-T SS). Flick switch → jumps between states. Bistability!
ON = high-T SS
Upper stable operating point:
high conversion, high temperature
OFF = low-T SS
Lower stable point: low
conversion, near feed temperature
Bistability + hysteresis
Path to SS depends on history:
ignition ≠ extinction temperature

## Slide 96
95
Packed Bed Pressure Drop
💡 Ceiling Lamp
Ergun: −dP/dz = 150μu(1−ε)²/(Dₚε³) + 1.75ρu²(1−ε)/(Dₚε³)
💡 Gas pushes UP through bulb filaments (packing). Pressure drops fighting through. Ergun quantifies.
Gas flow ↑ through bed
Superficial velocity u through
particle-packed column
Packing = resistance
Viscous (Blake-Kozeny) +
inertial (Burke-Plummer) terms
ε = void fraction
Bed porosity (0.35-0.5):
fraction of bed that is empty space

## Slide 97
96
PSSH & Rate-Determining Step
🪟 Glass Door
PSSH: d[I]/dt ≈ 0 | Rate = rate of RDS (slowest step)
💡 GLASS DOOR: see-through → intermediates transparent (pseudo-steady). RDS = how fast door opens.
See-through = PSSH
Reactive intermediate concentration
approximately constant
Door speed = RDS
Rate-determining step:
slowest elementary step = bottleneck
Solve for [I], simplify
Set d[I]/dt=0, eliminate [I]
from overall rate expression

## Slide 98
97
Enzyme Kinetics
🧺 Towel Rack
r = Vₘₐₓ · [S] / (Kₘ + [S]) [Michaelis-Menten]
💡 TOWEL RACK: hooks (enzyme active sites) grab towels (substrate). All hooks busy → Vₘₐₓ (saturated).
Hooks = active sites
Enzyme's catalytic sites:
limited number available
Towels = substrate [S]
Substrate concentration
determines reaction rate
Kₘ = [S] at r = Vₘₐₓ/2
Michaelis constant: substrate
conc. giving half-max rate
Lineweaver-Burk: 1/r = Kₘ/(Vₘₐₓ[S]) + 1/Vₘₐₓ

## Slide 99
98
Polymerization Kinetics
🧶 Bath Mat
Rₚ = kₚ·[M]·√(2Rᵢ/kₜ) | Chain growth
💡 BATH MAT: individual fibres (monomers) woven into long chains (polymer). Init → Prop → Termination.
Single fibre = monomer
Monomer [M] consumed in
propagation step
Woven mat = polymer
Growing chains build molecular
weight via propagation
Init → Prop → Term
Three stages: radical generation,
chain growth, chain termination

## Slide 100
100
Solving ODEs
💡 Floor Lamp
Euler: yₙ+₁ = yₙ + h·f(tₙ, yₙ) | RK4: 4 stages
💡 FLOOR LAMP: follow power cord from plug (t = 0) to bulb (t = final). Each cord step = Euler/RK step.
Plug (t=0) = initial cond.
Starting point y₀ at time
t₀ (known initial value)
Steps along cord = h
Step size h: smaller = more
accurate but more computation
Bulb = final answer
Solution y(tfinal) obtained
after marching through time

## Slide 101
101
Residence Time Distribution
💡 Floor Lamp
E(t) distribution | τ = V/Q | PFR: δ(t−τ) CSTR: e⁻t/τ/τ
💡 How long does each photon (molecule) stay in the room (reactor)? RTD = distribution of residence times.
Photon in = tracer injection
Pulse or step input of tracer
to characterize non-ideal flow
E(t) = exit age dist.
Probability distribution of
residence times in the reactor
σ² = spread/mixing
Variance measures departure
from ideal PFR or CSTR

## Slide 102
102
Polymerization Reactors
🪟 Window
Gel effect (Trommsdorff): viscosity ↑ → kₜ ↓ → auto-acceleration
💡 Watch polymer forming through window. Gel effect = window fogs up (viscosity ↑ dramatically).
Window fogs = gel effect
Viscosity increase slows
termination → rate accelerates
CSTR → Flory-Schulz MWD
Backmixed gives broader
MW distribution (PDI≈2)
PFR → narrow MWD
Plug flow: all chains see
same residence time → narrow PDI

## Slide 103
103
Batch Distillation
🗃 Fridge Drawer
Rayleigh: ln(L/L₀) = ∫dx / (y* − x)
💡 FRIDGE DRAWER: lighter volatiles float up first. Still pot gets heavier as lights are removed.
Light comp. rises first
More volatile component
enriched in distillate overhead
Pot gets heavier
Still pot composition shifts
toward less volatile as batch proceeds
Rayleigh tracks this
Integrate along VLE curve
to find remaining pot composition

## Slide 104
104
Multistage Distillation
🏗 Column (stairs)
y = R/(R+1)·x + xᴅ/(R+1) [Operating line]
💡 Climbing stairs (stages): each stair gets closer to pure product. More stairs or higher R = higher purity.
Each stair = 1 equil. stage
Equilibrium stage: leaving
streams in VLE
Higher R → more purity
Reflux ratio trades energy
cost for product purity
Fenske: Nₘᵢₙ at total R
Minimum stages at total
reflux (max separation power)

## Slide 105
105
McCabe-Thiele Diagram
💡 Wall Lamp
Rect: y = R/(R+1)·x + xᴅ/(R+1) | q-line for feed
💡 WALL LAMP illuminates McCabe-Thiele diagram. Count staircase steps between operating line and equil. curve.
Staircase = stages
Each step between op. line
and equil. curve = 1 stage
q-line: feed condition
q=1: sat. liquid feed
q=0: sat. vapor feed
Count steps = N stages
Graphical determination of
total theoretical trays needed

## Slide 106
106
Absorption Columns
🏭 Column
Z = NOG × HOG | NOG = ∫dy/(y − y*)
💡 Car wash: dirty gas flows up, clean solvent flows down. Each wash zone = 1 transfer unit. Counter-current!
Gas UP ↑
Gas phase flows upward
through packed column
Liquid DOWN ↓
Solvent flows down: absorbs
gas component at each height
Counter-current = max ΔC
Opposing flows maximize
driving force for mass transfer

## Slide 107
107
Stripping Columns
🗄 Corner Wall Cabinet
Stripping factor S = mG/L | S > 1 for effective stripping
💡 CORNER CABINET: strips out hard-to-reach dissolved gases from liquid. Reverse of absorption.
Dissolved gas = hiding
Dissolved solute in liquid
needs to be removed
Stripping = pulls out
Strip gas (steam, air) contacts
liquid to drive out dissolved gas
S > 1 → effective
Stripping factor > 1 ensures
enough driving force for removal

## Slide 108
108
Hunter-Nash (LLE)
🔺 Ternary triangle
F + S = R + E | Operating point on extended (F,S) line
💡 Ternary triangle = map. Operating point = compass bearing. Each extraction = one step on triangle.
Feed F
Feed mixture of solute
and carrier to be extracted
Solvent S
Immiscible solvent selectively
extracts the solute
Step between tie lines
Connect operating point through
tie lines to count stages

## Slide 109
109
Single-Effect Evaporator
☁️ Evaporator
F = L + V | F·xꜰ = L·xₗ | SE = V/S ≈ 0.8-0.9
💡 Single pot of soup: steam heats pot (F), water evaporates (V), soup concentrates (L).
Feed F in
Dilute solution entering
the evaporator
Vapor V out ↑
Water evaporated off:
driven by steam heating
Conc. liquid L out ↓
Concentrated product stream:
F·xꜰ = L·xₗ (solute balance)

## Slide 110
110
Multi-Effect Evaporator
☁️×3 Triple Effect
SE ≈ N (N effects → N times better steam economy)
💡 Three pots in series: steam from pot 1 heats pot 2, from 2 heats 3. Energy recycled between effects!
Effect 1: fresh steam
Live steam input: highest
T and P in the series
Effect 2: uses vapor from 1
Vapor from effect 1 serves
as heating medium for effect 2
Effect 3: uses vapor from 2
Cascading: each subsequent
effect runs at lower T and P

## Slide 111
111
Lumped Capacitance
🕯 Candle
T(t) = T∞ + (Tᵢ − T∞)·exp(−t/τ) | Bi = hLc/k < 0.1
💡 CANDLE: small object, uniform T everywhere (lumped). Blow out → T drops exponentially with time.
Small object = Bi < 0.1
Biot number small: internal
conduction >> external convection
Uniform T (lumped)
No spatial gradient inside:
whole object at one temperature
τ = ρVc/(hA)
Thermal time constant:
how fast object responds to T change

## Slide 112
112
Transient Conduction (Sphere)
🌐 Sphere
Fo = αt/r₀² | Bi = hr₀/k | One-term approx. + Heisler charts
💡 Sphere cooling: surface cools fast, center stays hot. Fo tracks how far heat has diffused inward.
Surface cools first
Convection removes heat from
outer surface immediately
Center stays hot
Internal conduction limits
how fast heat reaches center
Fo = αt/r₀²
Fourier number: dimensionless time
for conduction penetration depth

## Slide 113
113
Semi-Infinite Solid
🏔 Mountain
T(x,t) = Tₛ + (Tᵢ − Tₛ)·erf(x/√(4αt))
💡 Heat wave at surface penetrates deeper with time. Error function = how far the temperature front moved.
Surface: Tₛ applied
Sudden surface temperature change
at t=0 (step input)
Penetration δ ≈ √(αt)
Thermal penetration depth grows
with square root of time
Beyond 2√(αt): undisturbed
erf(2)≈1: material at depth
> 2√(αt) still at initial T

## Slide 114
114
Convection over Flat Plate
🏊 Flat Plate
Nuₓ = 0.332·Reₓ0.5·Pr¹/³ (laminar) | h = Nu·k/L
💡 Swimmer's hand: near wrist (leading edge) = thin laminar BL. Downstream fingertips → turbulent BL.
Leading edge: thin BL
Near plate start: laminar
thermal boundary layer develops
Downstream: turbulent BL
Beyond Reₓ ≈ 5×10⁵:
turbulent with higher h
Nu = hL/k
Nusselt number: dimensionless
heat transfer coefficient

## Slide 115
115
Free Convection
🌡 Radiator
Ra = Gr·Pr | Gr = gβ(Tₛ−T∞)L³/ν²
💡 Hot radiator: warm air rises (ρ↓), cold fills in below. Buoyancy ghost drives the flow. Gr = ghost strength.
Hot surface → ρ ↓ → rises
Thermal expansion reduces density:
buoyancy force drives upward flow
Cold fills in below
Cooler denser air replaces
rising warm air (natural circulation)
Ra < 10⁸: laminar
Rayleigh number determines
laminar vs turbulent free convection